## Slide 1: STARTER – ANSWER THE QUESTIONS

## Slide 2: B: The use of Digital Technology in designing and manufacturing processes

## Slide 3: By the end of this topic you should have developed a knowledge and understanding of:
CAD/CAM as used in industry
Testing, Modelling and Rapid prototyping
Stock Control, monitoring and purchasing logistics in Industry
High Volume production and Automation
The implications of the use of Digital Technology

## Slide 4: CAD CAM
C omputer
A ided
D esign
Computer
Graphics Tablet
Scanner (2D & 3D)
Internet Access
2D/3D software
C omputer
A ided
M anufacture
CNC lathe, Miller, router
Computerised embroidery
Laser Cutter
3D Printer
Plotter/cutter, vinyl cutter

## Slide 5: CAD. In the beginning…

## Slide 6: …and now?

## Slide 7: Computer Integrated Manufacture (CIM)
Designed on Computer
Prototype produced by 3D printer
Materials ordered and monitored by computer
Computer controlled machines make the product
Computer system monitors quality
Packaged and stored in warehouse by computer controlled vehicles

## Slide 8: Testing / Modelling
Why is this important?
Testing not only relates to testing of a product once it is made but can also relate to testing of a product in order to ensure it will work before it is made.
Testing can be about COMPUTER SIMULATION – this is useful in real-life situations where human testing is too dangerous.
Machine Processes can be simulated to test tool selection

## Slide 9: Mini Challenge
There is often limited seating in outdoor public spaces. There is a need for a product that can provide permanent seating yet be sensitive to the surroundings. The product should be suitable for a minimum of two people.
You will:
Write a Brief (5 mins)
Write a Specification (5 mins)
Draw at least 2 ideas (20 mins)
Model the best idea in SKETCHUP (30 mins)

## Slide 10: Homework
Evaluate your idea against your specification
Summarise its strengths and weaknesses
BRING TO LESSON TOMORROW

## Slide 11: Rapid Prototyping
Rapid prototyping can come in 3 main forms, Laminated Object manufacture,
stereo Lithography or Laser Sintering.
Rapid Prototyping is about TRANSLATING 3D CAD designs into SOLID physical forms. Different types of software is used to turn the 3D model into LAYERS. These layers can then be transformed into a solid prototype.
RP allows for the acceleration of design and manufacture. Although it means that the Designers spends longer on a product. As a result the CAD model must be right first time if it is also to be cost effective.

## Slide 12: Laminated Object Manufacture (LOM)
LOM is a very simple process that involves building up layers of ADHESIVE-coated material.
It is a very low cost processes due to readily available materials. It can be made to look like real materials. It can be made in large parts.
The process is performed as follows:
Sheet is adhered to a substrate with a heated roller.
Laser traces desired dimensions of prototype.
Laser cross hatches non-part area to facilitate waste removal.
Platform with completed layer moves down out of the way.
Fresh sheet of material is rolled into position.
Platform moves up into position to receive next layer.
The process is repeated
Processes Movie CLICK

## Slide 13: Stereo Lithography
Stereolithography is a common rapid manufacturing and rapid prototyping
technology for producing parts with high accuracy and good surface finish.
SL uses Resin and a laser to build the model. On each layer, the laser beam traces a part cross-section pattern on the surface of the liquid resin. Exposure to the UV laser light cures, or, solidifies the pattern traced on the resin and adheres it to the layer below. Typical Layer thickness is about 0.1mm and therefore a large model takes time to build.
Because models can be made in 1 day, money can be saved through JIT manufacture.
Models are also tough enough to be machined and can be used as patterns for Injection moulding etc..
Also there is no limitations on what shapes can be made.

## Slide 14: Laser Sintering
Selective laser sintering is an additive rapid manufacturing technique that uses a high power laser (for example, a carbon dioxide laser) to fuse small particles of plastic, metal, ceramic, or glass powders into a mass representing a desired 3-dimensional object.
The laser selectively fuses powdered material by scanning cross-sections generated from a 3-D digital description of the part (for example from a CAD file or scan data) on the surface of a powder bed.
After each cross-section is scanned, the powder bed is lowered by one layer thickness, a new layer of material is applied on top, and the process is repeated until the part is completed.

## Slide 15: 3D Printing
3D printing is a unique form of printing that is related to traditional rapid prototyping technology. A three dimensional object is created by layering and connecting successive cross sections of material. 3D Printers are generally faster, more affordable and easier to use than other additive fabrication technologies.
Like an Ink Cartridge the sytem prints ABS material in successive layers on top of each other to create the 3D image.
One variation of 3D printing consists of an inkjet printing system. Layers of a fine powder (plaster, corn starch, or resins) are selectively bonded by "printing" an adhesive from the inkjet printhead in the shape of each cross-section as determined by a CAD file. This technology is the only one that allows for the printing of full color prototypes. It is also recognized as the fastest method.

## Slide 16: Fused Deposition Modelling FDM
Process involves heating up plastic and squirting it onto a flat surface
The head moves around whilst the flat surface (bed) lowers layer by layer
Was patented in the 1980s but now open source
Large development community – downloadable products
Popular in schools and homes

## Slide 17: Stock control / Monitoring and purchase logistics
Stock control allows PRODUCTION to flow without any costly holds up, it allows sufficient raw materials and components to be readily available to ensure CUSTOMER DEMAND is met.
Stock control is now automated process. Computer systems using DIGITAL recognition technology can now be used to monitor stock.
Links are easily made to the purchasing department, marketing and sales departments to predict sales therefore allowing sufficient orders to be placed.
EDI = Electronic Date Interchange
This is a way in which data can be exchanged between computers within a company or between companies. It is used in Computer Stock Control systems. It uses agreed standard for product codes, prices and locaction allows for greater accuracy of stock control.
Advantages of Computer Stock Control
Lower staff costs
Improved efficiency and speed
No manual checks are needed
Efficiencies can lead to price reductions
Data can be presented in different ways for different people.
Date can be easily stored.
Disadvantages of Computer Stock Control
Initial high investment cost and training needed.
As only one person is needed QC can sometimes be lacking.
Software failure
Security.

## Slide 18: High-Volume Production
We have already touched upon this when talking about production techniques.
Benefits of Automated Systems
Low Labour costs
Low product costs because of the vast number of products being made
Consistent quality
QC checks are easy to carry out.
Benefits of Computer Stock Control
Drawbacks of Automated Systems
Drawbacks of Computer Stock Control
High Investment costs to set up
If the system breaks down it can be costly
Specialised workforce might be needed
Requires some flexibility in processing to enable manufacturing of different products.
Use your textbook(p103-104) to add some drawbacks/benefits in the boxes

## Slide 19: Computer Integrated Manufacture (CIM)
complete automation of a manufacturing facility such as a factory
Watch at end if time