## Slide 1: Forming and bending materials
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Forming and bending processes are those in which the shape of a material is changed by subjecting it to external forces. They include:
laminating
bending
pressing
forging
rolling.
© Wallingford

## Slide 3: Starter
How can you re-form the shape of resistant materials?
Think carefully about the times you have been in the workshop.
How many different ways have you used to re-form the shape of a piece of material?
Need a clue? – try CLAY!
© Wallingford

## Slide 4: Laminating (1)
In laminating, two or more layers of a material are bonded together to produce a single, larger section.
The process is usually used to produce:
a material that is longer, thicker or wider than is available in one piece, e.g. plywood, blockboard
a section that cannot be cut from a single piece of material, e.g. a curved beam
a section with improved properties, e.g. the stability of synthetic boards or the heat and water resistance of Formica.
© Wallingford

## Slide 5: Laminating (2)
Timber
Thin layers of timber (veneers) are built up in layers in a former to make a light, strong form.
Each layer of veneer is laid into the former with its grain at right angles to the previous layer in order to increase the structural strength of the product.
While the glue between each layer is wet the sandwich can be bent into shape by the application of pressure, using either a vice or a bag press.
When the glue has set, the sandwich will retain its curved shape.
© Wallingford

## Slide 6: Laminating (3)
Thermoplastics
Layers of paper or fabric are impregnated with thermosetting resins such as phenol formaldehyde, and compressed under high pressure and heat.
Examples of thermoplastic laminates include:
Formica, which is used to make kitchen worktops
Tufnol, which is used to make printed circuit boards.
© Wallingford

## Slide 7: Laminating (4)
Glass-reinforced plastic (GRP)
Layers of glass fibre are impregnated with polyester resin to produce a lightweight, strong and hardwearing material.
GRP can be used to manufacture products that range in size from boat and car body shells to children’s toys.
Weight for weight, GRP is stronger than steel, and has excellent resistance to corrosion.
Carbon fibre
This is used in a similar way to GRP, but it is even stronger and lighter, providing an exceptional strength-to-weight ratio.
© Wallingford

## Slide 8: Bending
Bending is subdivided into two groups:
Single curvature bending – a material is either bent cold, or heated until it becomes pliable and bent to shape over simple formers or jigs in one direction only.
Compound curvature bending – a material is either bent cold, or heated until it becomes pliable and formed in two or more directions at the same time, to make dished shapes.
© Wallingford

## Slide 9: Single curvature bending (1)
Line bending: plastics
A strip heater is used to heat thermoforming plastics such as acrylic along an narrow line, enabling it to be bent to a desired angle.
When heating the material, it should be turned over in order to heat it evenly and avoid burning it.
Greater accuracy and consistency is achieved by using a bending jig.
© Wallingford

## Slide 10: Single curvature bending (2)
Line bending: metal
Folding bars are used to bend thin sheet metal along a straight line.
The material is placed between the bars, which are then clamped together. The protruding material can then be bent accurately along its length by tapping it with a rawhide mallet.
Box folders are used to bend thin sheet metal along a straight line.
The material is placed between the bars, which are then clamped together. The protruding material can then be bent accurately along its length, either manually or (as in industry) in a powered operation.
© Wallingford

## Slide 11: Compound curvature bending (1)
Vacuum forming
Vacuum forming is used to form thin plastic sheet material such as polystyrene, ABS, PVC and acrylic. The material is clamped in the machine and heated until it becomes pliable. The former is raised and the vacuum applied: this draws the material down tightly over the former.
Formers must have draft angles, and rounded corners and edges, in order to release the material after forming.
Vacuum forming is a relatively low cost process because the former is cheap to make. It is used to manufacture packaging items such as egg boxes, yoghurt pots and microwave meal trays.
© Wallingford

## Slide 12: Compound curvature bending (2)
Dome blowing
Dome blowing is used to form sheet plastics into domed shapes.
The material is clamped in the machine beneath a sheet of metal with a hole in it, and heated until it becomes pliable.
Air is blown up into it, causing a dome to rise.
Dome blowing is a relatively low-cost process because the former is cheap to make.
© Wallingford

## Slide 13: Compound curvature bending (3)
Press forming: plastics
Press forming is used to form thicker sheet plastics, such as acrylic, into dish shapes.
The material is heated in an oven for 20 to 30 minutes at 165°C.
It is then placed on the female part of the former, and the male part is then pushed into it to form the dish.
Press forming is a relatively low cost process, because the wooden former is cheap to make.
© Wallingford

## Slide 14: Compound curvature bending (4)
Press forming: metal
This is used to form sheet and strip metals into disc or dish shapes by punching or pressing.
Punching: the metal blank is placed over the female part of the former (die), and the male part (punch) is then forced through it to form the desired shape.
In industry, large presses that exert forces measured in tonnes are used to punch the material.
On CNC-controlled machines, sheets of material are moved around the bed beneath the punching tool.
Items such as metal cabinets, washers, bicycle chain links and coinage are manufactured in this way.
© Wallingford

## Slide 15: Compound curvature bending (5)
Press forming: metal
Pressing: used to form thin sheet metals into dish shapes. The material may have to be annealed prior to forming if it is too hard.
The metal blank is placed over the female part (die) of the former, and the male part (punch) is then forced into it to form the object.
This may have to be carried out in a series of steps in order to avoid overstretching and tearing the material.
In industry, large presses that exert forces measured in tonnes are used to manufacture car body panels, stainless steel kitchen sinks and metal containers, ranging from food cans to saucepans.
© Wallingford

## Slide 16: Compound curvature bending (6)
Spinning
Spinning is used to form thin sheet metals such as stainless steel and aluminium into circular dish shapes. It is a widely applied mass production process, used to produce bowl-shaped kitchenware.
A metal disc is mounted in a lathe between a former and a tailstock pad, which revolve with it. A rounded steel bar is pushed against the disc to push it over and form the dish. The material may have to be annealed prior to forming in order to soften it.
Spinning is a relatively low cost process.
It is a dangerous process, which should not be carried out in schools.
© Wallingford

## Slide 17: Compound curvature bending (7)
Beaten metalwork
This is used to form thin sheet metals such as copper, brass, gilding metal, silver and gold into hollow shapes such as jugs, and in jewellery manufacture. It is one of the oldest metalworking craft processes, and is usually used to produce one-off items.
A thin metal disc is beaten into shape with a mallet or hammer by either hollowing, sinking or raising.
Although the tooling costs are low, the cost of manufacture is high because of the high level of skill and the time required to make an object.
© Wallingford

## Slide 18: Compound curvature bending (8)
Beaten metalwork
Hollowing is a method of shaping bowls by beating sheet metal into a sandbag with a bossing mallet.
Sinking is similar to hollowing; the centre of a disc is sunk, leaving a margin, which becomes a flat rim.
Raising is used to achieve deeper forms than possible by either hollowing or sinking. The disc of metal is hammered on the outside while resting against a metal stake.
© Wallingford

## Slide 19: Compound curvature bending (9)
Beaten metalwork
Planishing is the process by which the surface of objects produced by hollowing, sinking and raising are trued up, and hammer marks are removed.
A flat or slightly domed hammer with a polished face is used to trap the work between the face and an appropriately shaped stake, which should also be highly polished.
Planishing marks are usually buffed out. However, if planishing is carried out carefully, a faceted, decorative pattern is achieved.
© Wallingford

## Slide 20: Compound curvature bending (10)
Beaten metalwork
Seamed and box work is a method of creating three-dimensional forms from sheet metal.
A net is cut from the sheet metal, and the edges are soldered together.
If a number of pieces are to be joined together by soldering it is important to use solders with progressively lower melting points as each piece is added.
The soldered form is then beaten to produce the finished form.
© Wallingford

## Slide 21: Compound curvature bending (11)
Beaten metalwork
Work hardening: As the metal is shaped by hammering its internal structure changes, and it becomes hard. This makes it increasingly difficult to work.
Annealing allows the stress that has built up in the structure to relax and return to its initial form. This is achieved by heating up the metal and allowing it to cool.
Pickling is used to remove the oxidization deposits caused by heating the metal. The cooled metal is dipped into dilute sulphuric acid to remove the scale. Brass tongs should always be used.
© Wallingford

## Slide 22: Forging (1)
Forging is the heating of metal and either hammering it to form new shapes or applying forces to bend or twist it.
The metals usually shaped by forging are black mild steel and tool steel.
It is used to produce strong and tough forms. When the material is hammered the grain structure is refined, and so the toughness increases.
Correct forging results in a component in which the grain structure follows the shape without breaks, making it stronger than the same thing manufactured by machining.
© Wallingford

## Slide 23: Forging (2)
Forging as a craft process offers great opportunities for highly original and creative designs.
There are few traditional blacksmiths working today, and forging has developed into a sophisticated CNC-controlled process.
Drop forging uses two halves of a die, between which hot metal is squeezed into the required shape.
A powered hammer is used to exert forces measured in tonnes to forge components such as crankshafts, bolt heads, knives and turbine blades.
© Wallingford

## Slide 24: Forging (3)
The forge is used to heat the metal to the correct temperature – mild steel to 1200°C (red/yellow heat) and tool steel to 900°C (red heat).
A traditional blacksmith’s forge uses coke as fuel, and the intensity of the fire is achieved by blowing air into it with bellows.
Today gas-fired ceramic forges are used; the ceramic chips are heated by the gas burner, and glow red in a similar way to the coke in the traditional blacksmith’s forge.
© Wallingford

## Slide 25: Forging (4)
The anvil is made from mild steel with a hardened steel working face welded to it.
The cutting face is used for rough work, general forming and cutting metal against. One edge is rounded for making radiused bends.
The hardie hole is for mounting various forging tools (hardies, fullers and swages) and the punching hole is for creating holes.
The bick is used for forming curves.
© Wallingford

## Slide 26: Forging (5)
© Wallingford
Hammers
Ball pein hammers of different weights from 0.5kg to 1kg are used to work the hot metal.
A sledgehammer is used for very heavy work.

## Slide 27: Forging (6)
Tongs
Tongs are used to handle short lengths of hot metal.
The mouth is shaped to hold different sections, e.g. open for flats, round and square.
Flatters
Flatters are used to smooth the metal surface after initial working.
The workpiece is trapped between the face of the anvil and the flatter, which is struck with a hammer.
© Wallingford

## Slide 28: Forging (7)
© Wallingford
Fullers and swages
Fullers and swages are used in pairs to draw material down to size.
The bottom fuller fits in the hardie hole of the anvil, and the top fuller is struck with a hammer.
Swages are used to shape metal.

## Slide 29: Forging (8)
© Wallingford
Chisels
Chisels are used to cut metal to length. There are two types: hot and cold.
Hot chisels are thinner, and cut more easily into hot metal. They are also longer, so that the smith can keep his hands away from the hot metal.
A hot chisel should be regularly quenched in water in order to maintain its temper.

## Slide 30: Rolling
© Wallingford
Rolling is one of the most widely used forming processes.
It consists of passing a piece of metal between a series of rollers in order to reduce it to a specific thickness.
Rolling mills usually form part of a steelworks, where rolling is used to produce sheet, strip and metal foil.
Rolling is also used to produce profiled sections, such as railway track, and structural steel.
In school, considerably smaller benchtop roller sets can be used in a similar way to form small sections of metal.

## Slide 31: Tasks
Task 1: Name and describe the five methods of forming and bending
resistant materials. Use Worksheet 1.
Task 2: Describe in detail one method: vacuum forming. Use
Worksheet 2. Your description should include:
a labelled picture of a vacuum forming machine
a step-by-step description of the process.
© Wallingford

## Slide 32
How is a blister pack made?
Write a paragraph explaining the making of blister packs.
What are they used for?
How many blister pack products can you name?
© Wallingford