## Slide 1: Computer-aided design
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Computer-aided design (CAD) is the use of computers as a design tool.
Specialized CAD software exists for many sorts of design: architectural, engineering, electronics, structural, clothing etc.
Almost every product we buy today has been designed and engineered using CAD.
A CAD system is made up of hardware and specialist software.
CAD systems also require: a high-quality graphics monitor; a mouse, light pen or digitizing tablet for drawing; and a high-resolution printer or plotter for printing design drawings.
© Wallingford

## Slide 3
© Wallingford
INPUT
Keyboard
Light pen
Digitizing tablet
Scanner
PROCESS
High-end
computer with
graphics card
OUTPUT
Monitor
Printer
Plotter
Digital
Introduction

## Slide 4: Starter
What do the letters CAD stand for?
Who uses CAD?
What do they use it for?
© Wallingford

## Slide 5: Computer-aided design
© Wallingford
CAD involves the inputting of lines, arcs, coordinates, dimensions and text for engineering purposes into a database.
The advantage of this is the ability to manipulate the data in many ways during and after completion of a design.
CAD software can be used to create two-dimensional (2D) drawings or three-dimensional (3D) models.

## Slide 6: 2D computer-aided design
© Wallingford
2D CAD is very like drawing on a traditional drawing board.
The drawings produced are essentially flat views, which can be dimensioned, or basic 3D drawings in isometric.
TechSoft 2D Design is an example of 2D CAD software used in many schools.

## Slide 7: 3D computer-aided design (1)
© Wallingford
3D CAD enables the creation of virtual models, with the ability to manipulate them as if they were actual solid objects.
Each 3D model is an exact replica of the design in digital format, which can be scaled up or down and modified to any specific tolerance.
3D CAD software allows designers to view a design from any angle, with the ability to zoom in or out for close-ups and long-distance views.

## Slide 8: 3D computer-aided design (2)
© Wallingford
3D CAD software keeps track of design dependencies, so that when the designer changes one value, all other values that depend on it are automatically updated.
Pro/DESKTOP, SolidWorks and ArtCAM are examples of 3D CAD software used in many schools.
3D CAD model of a mobile phone case produced using Pro/DESKTOP

## Slide 9: 2D CAD in school (1)
The drawings on this slide and the next were produced using the TechSoft 2D Design CAD drawing package.
Drawing No. 1 is a third angle orthographic drawing, from which the student was able to manufacture the CD rack.
Drawing No. 1

## Slide 10: 2D CAD in school (2)
In Drawing No. 2, the CAD file that was used to produce Drawing No. 1 has been modified to produce the rendered version.
Drawing No. 2
© Wallingford

## Slide 11: 2D CAD in school (3)
The drawing on the right has been produced using the original CD rack CAD file and has:
– been re-scaled to 1:1 (full size)
– had unwanted views deleted
– had graphics added to it
– been copied and pasted
– been nested together in order to make the best use of the material by minimizing waste.
The black lines will be cut through.
The red areas will be engraved.
The drawing will enable the shelves to be made in acrylic by using a laser cutter to engrave and cut them out.
© Wallingford

## Slide 12: 3D CAD in school (1)
The drawings on the right were produced using a 3D CAD drawing package – Pro/DESKTOP.
In 3D CAD all the parts that make up the product are drawn full size, as in the drawings on the left.
The parts are then assembled to make a virtual image of the product. If the parts are the wrong size in any way, they will not fit together.
© Wallingford

## Slide 13: 3D CAD in school (2)
Once the assembly drawing has been successfully completed it is possible to produce working drawings and rendered impressions of the finished product using the same data – they do not have to be drawn again.
The drawing on the right is a third angle orthographic working drawing, generated using the assembly drawing.
© Wallingford

## Slide 14: 3D CAD in school (3)
The drawing on the right is a wireframe drawing of the CD rack.
It was generated from the assembly drawing by simply pressing one button.
Wireframe drawings are useful, because they allow us to look inside the product and see how parts meet together.
© Wallingford

## Slide 15: 3D CAD in school (4)
The drawings on the right are rendered views of the CD rack.
They have been generated from the assembly drawing.
Rendered drawings are useful, because they allow us to look at the product from different angles, and to change the colour to see how the finished product would look in a range of colour schemes.
© Wallingford

## Slide 16: 3D CAD in school (5)
The drawings on the right show a turbine that is to be milled directly out of a block of aluminium.
This same software can be used to design formers for vacuum forming and patterns for casting.
The original CAD drawing has to be sent to another program that converts it into a CAM file.
© Wallingford

## Slide 17: CAD in architecture
Architects use CAD to plan buildings.
For any architectural project a series of drawings has to be produced, first to obtain planning consent and then to provide information to the builder about how the project is to be constructed and finished.
These drawings include:
– site plans
– building plans
– building elevations
– service diagrams
– detail drawings
– rendered views.
© Wallingford

## Slide 18: CAD in interior design
Interior designers use CAD to plan and view interior spaces. Whether it is a simple, small bedroom or a complex interior such as an entertainment complex, all the fittings can be inserted into the space and viewed from various angles.
Interior designers use a library of fixtures and fittings, which are simply selected and positioned in the appropriate position in the space.
© Wallingford

## Slide 19: CAD in electronics
The microelectronics revolution has been made possible by the use of CAD.
Circuits are designed using software built round a library of components.
The designer builds a virtual circuit using components from the library, and tests it on screen to see if it works.
Once the circuit has been designed and proven, it is converted using CAD into a PCB track layout suitable for manufacture.
© Wallingford

## Slide 20: CAD in structural engineering (1)
Structural engineers use sophisticated CAD software to build and test structures.
Individual structural elements are created, then assembled and finally tested on screen.
The structure is then tested by rigorous structural analysis by subjecting it to loading in a range of forms.
It is even possible to simulate earthquakes and high winds.
© Wallingford

## Slide 21: CAD in structural engineering (2)
West Point Bridge Designer is an example of a structural engineering CAD program. It can be downloaded free from the Internet.
It enables a range of different bridges to be designed and tested on screen by simulating a truck driving over them.
As the truck passes over, the structural members change to red or blue, depending on whether they are in tension or compression.
The hypothetical cost is calculated as the material and size of each member is altered. If the bridge is poorly designed it will collapse.
The challenge is to produce the most cost-effective design.
© Wallingford

## Slide 22: CAD in services engineering
Buildings and vehicles have become increasingly sophisticated.
The services that run in both include electrical, heating and ventilation, communication, and plumbing.
All these services have to be routed.
Services engineers use sophisticated CAD software to plan the routes for services.
Once planned, the system can be tested on screen and any faults rectified before installation has started, thereby saving potential lost time and money.
© Wallingford

## Slide 23: CAD in mechanical engineering
Almost every product we purchase today has been engineered using CAD.
Engineers use CAD software such as AutoCAD to model complex designs ranging in scale from a small plastic toy to an oil refinery.
In both cases the CAD system gives the precision required to ensure that:
– all the component parts will fit together
– tooling required for manufacture can be produced.
© Wallingford

## Slide 24: CAD and virtual reality
Software now exists to enable designers and their clients to put on headsets and walk through virtual environments, or sit in virtual cars and simulate the driving experience.
This highly advanced CAD application is extremely expensive.
It requires enormous processing power if a real-time virtual experience is to be achieved.
© Wallingford

## Slide 25: Advantages of using CAD
CAD allows designers to model and compare designs quickly and cheaply.
CAD drawings can be sent to any part of the world electronically using email.
CAD drawings can be edited quickly without having to redraw them.
CAD systems enable designers to assemble components on screen and test whether the design will work.
© Wallingford

## Slide 26: Tasks
Task 1: What do designers use CAD for? Look at the list of designers and CAD applications on the worksheet. Draw up a table identifying which designer used which technique.
Task 2: When you have done this, create a mind map that summarizes the ways in which CAD is used by different people as part of the design process.
© Wallingford