## Slide 1: Casting and moulding
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Casting and moulding are among the oldest techniques for forming products.
Originally developed around 5000 years ago to form metals into basic tools and weapons, today similar techniques are used to form plastics.
They have lasted so long in a relatively unchanged form as manufacturing techniques because they can be used on most metals and plastics to produce complex products in a single operation.
The quality of the end product is often so high that no further finishing is required.
The process of casting and moulding can be broken down into three basic stages:
Solid material is heated and becomes liquid.
Liquid material is poured into a mould.
Liquid material cools and returns to a solid state.
© Wallingford

## Slide 3: Starter
What do you understand by the terms casting and moulding?
How many different forms of casting and moulding can you name?
© Wallingford

## Slide 4: Casting
Casting is the term used to describe the pouring of molten metal and thermosetting plastic resins into moulds.
Casting
Sand
casting
Die
casting
Cold
resin
Investment
casting
© Wallingford

## Slide 5: Sand casting (1)
Sand casting is used in industry for small-batch production runs, and large or intricate castings.
Complex shapes such as taps would be almost impossible to produce by any other method.
In split pattern casting a pattern of the object to be cast is manufactured from timber, such as jelutong or MDF.
The pattern is used to create a cavity in moulding sand; it is then removed, and molten metal is poured into the cavity.
© Wallingford

## Slide 6: Sand casting (2)
In lost pattern casting a pattern is made from polystyrene foam.
The pattern is left in the moulding sand; when the molten metal is poured the pattern is burned out, leaving a cavity for the metal to fill.
A crucible furnace is used to melt metal.
Today gas is the usual source of heat, but they can also be fired by coke and oil.
The metal charge is introduced into the crucible in the form of broken ingots and scrap from previous castings.
All metal added to the crucible must be warmed first and completely dry, in order to avoid splashes of molten metal.
© Wallingford

## Slide 7: Sand casting (3)
© Wallingford
The moulding flask is usually made of cast iron, and comes in two parts: the lower drag and the upper cope.
Sprue pins are wooden pegs that are used to make the vertical channels in the sand down which the molten metal will flow.
Moulding sand must be able to withstand the heat, allow gases to escape, and hold its shape.
A rammer is used to compact the sand in the moulding box.

## Slide 8: Sand casting (4)
© Wallingford
Moulding tools are used to form pouring pools and gates into and along which the molten metal flows.
Personal protective equipment: it is important that appropriate PPE is worn when pouring molten metal.
Leather gaiters, gauntlets, gloves and apron plus a full face mask are essential.

## Slide 9: Sand casting (5)
© Wallingford
Split pattern casting: step by step
Place the drag on the moulding board and place half of the split pattern in the centre. Sprinkle with parting powder.
Fill the drag with sieved moulding sand, which should be rammed down well. When full, strickle off with a piece of metal bar.
Turn the drag over and sprinkle with parting powder.

## Slide 10: Sand casting (6)
Split pattern casting: step by step
Fit the cope over the drag, and fit the upper half of the pattern to the lower half.
Install the sprue pins, fill the cope with sieved sand, ram down well, and strickle off.
Remove the sprue pins and create a pouring basin that links to the runner. All loose sand should be blown away and a rounded lip between the pouring basin and the runner formed.
© Wallingford

## Slide 11: Sand casting (7)
© Wallingford
Split pattern casting: step by step
Separate the cope and drag, and then cut gates from the sprue to the pattern, and from the pattern to the riser, to enable the metal to flow through to the mould.
Reassemble the cope and drag.
Pour molten metal into the pouring basin and allow it to flow through the mould until it can be seen coming up the riser.
Allow to cool and knock out the casting.

## Slide 12: Sand casting (8)
© Wallingford
Lost pattern casting
The process of preparing a lost pattern casting is similar to that for the preparation of a split pattern casting.
The difference is that there is no need to remove the foam plastic pattern, because it is burned out as the metal is poured in.
Great care needs to be taken when lost pattern casting because of the toxic fumes given off by the burning plastic.

## Slide 13: Die casting (1)
Die casting is used to manufacture metal products in large quantities.
Unlike sand casting, where the cope and drag have to be separated and remade after each casting, die casting uses a steel mould that can be used repeatedly.
Die casting uses low melting point metal alloys such as aluminium, zinc and pewter.
There are two basic methods of die casting:
– gravity die casting
– pressure die casting.
© Wallingford

## Slide 14: Die casting (2)
Gravity die casting
In gravity die casting, gravity is the force that ensures the flow of the molten metal into and around the metal mould.
It is a low-tech process that is well suited to the batch production of simple forms without undercuts.
Molten metal is ladled manually into simple, welded steel moulds.
Gravity die casting requires minimal finishing; waste is minimal because excess metal can be melted down and used again.
© Wallingford

## Slide 15: Die casting (3)
Pressure die casting
In pressure die casting a hydraulic ram is used to force a shot of molten metal into and around the metal mould.
It is a high-tech process that is well suited to the mass production of precise complex forms.
Pressure die casting requires minimal finishing, and waste is minimal because any excess metal can be re-melted and used again.
© Wallingford

## Slide 16: Die casting (4)
Pressure die casting
Pressure die casting can produce castings with accuracy comparable to machining tolerances.
Typical precision of 0.025mm in 25mm is possible – i.e. 0.1% of the dimension.
Once tolerances have been achieved, they are set for life, giving long-term production consistency.
This has tremendous benefits for automated assembly processes where consistent accuracy is vital, e.g. automobile assembly lines.
© Wallingford

## Slide 17: Die casting (5)
Pressure die casting
The moulds are called dies and are made from steel. A very high level of detail can be achieved; however, this means that dies are very expensive to manufacture.
A die casting die set must be able to:
hold molten metal in the shape of the final casting
provide a path for the molten metal
remove heat from the casting
eject the solidified casting
withstand forces measured in tonnes when closed.
© Wallingford

## Slide 18: Die casting (6)
Pressure die casting: step by step
© Wallingford

## Slide 19: Die casting (7)
Pressure die casting: step by step
When the process has been completed, the runners and risers plus any flash are removed.
This is called fettling.
The parts are then finished. Die castings require minimal finishing because of the high quality that can be achieved.
If a colour finish is required, this can be achieved by anodising or powder coating.
© Wallingford

## Slide 20: Investment casting (1)
Investment casting, also called lost wax casting, is one of the oldest metal-forming techniques, dating back around 5000 years, when beeswax formed the pattern.
Today high-technology waxes, refractory materials and specialist alloys are used.
© Wallingford

## Slide 21: Investment casting (2)
Investment casting enables the repeated production of components with high accuracy, in a variety of metals and high-performance alloys.
The process is used for small castings. It is generally more expensive per unit than other casting methods.
Investment casting is used to produce complicated shapes that would be difficult or impossible with die casting, and requires little surface finishing.
© Wallingford

## Slide 22: Investment casting (3)
A pattern of the component to be cast is produced by injection-moulding special wax into a metal die.
Preformed ceramic cores can be included in the wax pattern as it is moulded, which can create intricate hollows within the finished casting.
The wax patterns are assembled into a tree around a wax runner. Once a tree has been assembled, a pour cup is attached.
© Wallingford

## Slide 23: Investment casting (4)
The completed tree is dipped, or invested, by hand or via robotic control into a ceramic slurry.
A fine sand is applied to the invested tree.
The tree is then allowed to dry before re-dipping in slurry.
This process is repeated until the shell is thick enough to withstand the mechanical shock of receiving the molten metal.
After the shell has been constructed, the wax is removed in an autoclave or furnace – hence the name ‘lost wax process’.
The shell is then fired at temperatures of around 1100°C to produce a ceramic shell of the part to be cast.
© Wallingford

## Slide 24: Investment casting (5)
Most foundries remove the shells from the furnace while still hot and pour the molten metal into the ceramic shell.
There are various methods of pouring the molten metal, including vacuum casting, gravity pouring, pressure-assisted pouring, and centrifugal casting.
After the molten metal cools, the shell is removed by vibration, grit-blasting or chemical dissolution.
When the parts have cooled, they are removed from the tree by sawing them free, or by dipping them in liquid nitrogen and breaking them off with a hammer and chisel.
The parts are then finished (see next slide).
© Wallingford

## Slide 25: Finishing metal castings (1)
Because molten metal cools slowly, cast parts do not finish as hard as parts produced by some forging and machining processes.
If required, cast parts can be subsequently hardened by heat treatment, surface hardening, or HIP (hot isostatic pressing) hardening.
Following the removal of sprues, castings are then accurately finished using a variety of tools and machines.
Secondary machining processes such as drilling, tapping and milling are carried out as required to meet the product specification.
© Wallingford

## Slide 26: Finishing metal castings (2)
Components can be bead-blasted to clean surfaces before polishing.
This involves blasting abrasive grits onto the surface of the casting using compressed air.
The final part of the finishing process is to polish the castings in a vibratory polishing machine, where the component is tumbled in ceramic pyramids.
The finished parts are given a final inspection by eye or, in special cases, by X-ray to ensure that they meet the appropriate quality standards, prior to dispatch.
© Wallingford

## Slide 27: Cold resin casting (1)
Polyester and epoxy resins can be cast into solid blocks, which can then be used as cast, or worked by machine and hand tools as for metal castings.
Clear polyester resin castings are used to embed objects to make decorative objects such as jewellery and paperweights.
By adding pigment the colour of the object being cast can be changed.
To achieve a casting with high-quality finish, moulds must also have a smooth finish and a draft angle to remove the object being cast after curing.
© Wallingford

## Slide 28: Cold resin casting (2)
Prepare the mould by applying a release agent to prevent the cured object from sticking to it.
Prepare the casting resin by adding the catalyst or hardener and mix thoroughly.
Pour the resin carefully into the mould to avoid creating air bubbles.
Allow to cure.
If embedding an object to produce a paperweight, repeat this process in layers until the mould is full.
© Wallingford

## Slide 29: Moulding
Moulding is the term used to describe the melting of plastics and
reforming them.
Moulding
Injection
moulding
Rotational
moulding
Compression
moulding
Calendering
Blow
moulding
Extrusion
© Wallingford

## Slide 30: Extrusion (1)
Extrusion is the term used to describe the process of forcing a material through a die to produce both solid and hollow shapes.
The principle of extrusion is similar to the way toothpaste is squeezed from a tube.
Extrusion can be used to form metals, plastics and woodcrete.
Commonly used materials include aluminium, ABS, acrylic, PVC, polycarbonate, polypropylene, HIPS, polystyrene and polyurethane.
© Wallingford

## Slide 31: Extrusion (2)
Extrusion is a continuous process, producing sections at between 6 and 60 metres per minute, depending on the thickness of the section being extruded.
For example, the external sheathing around electric cables is extruded around the cable as it is passed through the centre of the die.
Extruded sections can be designed to interlock mechanically, e.g. electric trunking and UPVC window frames.
© Wallingford

## Slide 32: Extrusion (3)
Extruding plastics
Thermoplastic granules are fed from a hopper into the chamber, where they are fed along the barrel by an archimedes screw.
As the granules pass along the barrel they are heated and become plasticized (liquid).
The plasticized material is then forced through a die to form the section being manufactured.
The extruded section is cut to stock lengths for storage and transportation.
© Wallingford

## Slide 33: Injection moulding (1)
Injection moulding is similar to extrusion, but the archimedes screw is replaced by a plunger that injects a shot of molten plastic into a mould.
It is the equivalent of die casting in metal.
Injection-moulded products have a high level of finish and detail on both the internal and external surfaces.
© Wallingford

## Slide 34: Injection moulding (2)
The process is expensive to set up because of the high cost of producing the mould.
However, once in production the unit cost per component in terms of material and labour is very low.
Commonly used materials include ABS, acrylic, PVC, polycarbonate, polypropylene, HIPS and HDPE.
© Wallingford

## Slide 35: Blow moulding (1)
Extrusion blow moulding begins in a similar way to extrusion.
A tube of plastic is extruded between two halves of a mould.
The mould then closes, sealing the base, and air is blown in to inflate the tube to the internal shape of the mould.
Extrusion blow moulded products have a high level of finish and detail on both the internal and external surfaces.
© Wallingford

## Slide 36: Blow moulding (2)
The process is expensive to set up because of the high cost of producing the mould.
However, once in production the unit cost per component in terms of material and labour is very low.
Commonly used materials include ABS, acrylic, PVC, PET, polypropylene, HIPS, LDPE and HDPE.
© Wallingford

## Slide 37: Blow moulding (3)
Film blow moulding begins in a similar way to extrusion.
A continuous tube of plastic is extruded and blown into an extremely large bubble, which can reach heights of 10m plus.
The bubble, which is blown vertically, stretches the plastic into a thin film that, as it cools, is wound round a roller to produce long, wide sheets of plastic.
© Wallingford

## Slide 38: Blow moulding (4)
The process is expensive to set up because of the high cost of equipment.
However, once in production the unit cost per linear metre in terms of material and labour is very low.
The most commonly used material is polythene.
© Wallingford

## Slide 39: Rotational moulding (1)
Rotational moulding is a very flexible manufacturing process in terms of both the shape and the size of products that can be made.
It is used to manufacture complex one-piece mouldings, from hand-held products such as dolls’ heads and footballs through to large storage tanks.
Rotational moulding has significant economic advantages over other moulding processes, mainly because of the low tooling costs.
This enables low-volume production runs to be carried out.
© Wallingford

## Slide 40: Rotational moulding (2)
The process involves pouring a shot of thermoforming plastic into a hollow mould.
The mould is then rotated in two directions while being heated in an oven.
The molten plastic forms a thin, even layer on the inside of the mould as it rotates.
© Wallingford

## Slide 41: Compression moulding (1)
Compression moulding is a way of forming thermosetting plastics.
It is used to manufacture products such as electrical fittings from urea formaldehyde, bottle tops from phenol formaldehyde, rigid plastic crockery from melamine formaldehyde, and footwear soles from synthetic rubber.
© Wallingford

## Slide 42: Compression moulding (2)
The process involves placing a shot of powdered thermosetting plastic into a heated hollow mould.
The mould is then closed and the combination of heat and pressure forces the plasticized powder to take the shape of the mould.
The operating temperature is around 200°C, and the force applied to the mould when closed ranges from 20 to several hundred tonnes, depending on the size of the product being manufactured.
© Wallingford

## Slide 43: Calendering (1)
Calendering is used to manufacture plastic sheet materials such as packaging films, adhesive tapes and washable wallpapers.
Plasticized material is passed through a series of heated rollers that make it progressively thinner as it passes through each set.
Calendering can produce rolls of material several metres wide and between 0.05mm and 1.3mm thick.
© Wallingford

## Slide 44: Calendering (2)
If a textured surface is required the material is passed through a set of heated embossing rollers.
If the material is to be bonded to a backing sheet for use as wallpaper, or if it requires a peelable backing, this is fed through a separate set of rollers and the two are bonded or attached at the end of the process.
© Wallingford

## Slide 45: Tasks
Summarize the different methods of casting and moulding in a table.
Use Worksheet 1.
Your table should include details of:
– process name
– materials used
– products made.
Following a demonstration, describe in detail the process of cold resin casting.
Use Worksheet 2.
Your description should include details of:
– mould design
– materials used
– a step-by-step description of the process.
© Wallingford