## Slide 1: Computer-aided manufacture
© Wallingford
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Computer-aided manufacture (CAM) is the use of computers as a manufacturing tool.
Specialized CAM machines are able to carry out a range of manufacturing processes.
Some of these are subtractive (things are removed), and some are additive (things are put together).
A CAM system is made up of computer hardware, and the specialist software required to process CAD-generated CNC data.
CAM systems require manufacturing machinery such as robots, lathes, millers, lasers, routers and plotter/cutters to carry out their tasks.
© Wallingford

## Slide 3: Introduction
© Wallingford
INPUT
CNC data
PROCESS
CAM
machine
OUTPUT
Product

## Slide 4: Starter
What do you understand by the term computer-aided manufacture?
List 20 products produced using CAM.
© Wallingford

## Slide 5: Computer numerical control
© Wallingford
CAM is the process of manufacturing products using data received from a CAD package.
The link between CAD and CAM is computer numerical control (CNC). CNC enables the lines on a drawing or model created in a CAD program to be converted into movements of a CAM machine tool.
The CNC machine codes generated are not seen by the CAM machine operator. For example, the only decisions that have to be made before switching on a CNC milling machine are:
– the cutting speed
– the cutting tool to be used
– the depth of cut.

## Slide 6: Subtractive and additive CAM
CAM manufacturing processes can be divided into two broad groups: subtractive (things are removed) and additive (things are put together).
Subtractive processes include:
– turning
– milling
– routing
– cutting
– punching.
Additive processes include:
– assembly
– welding
– painting
– rapid prototyping.
© Wallingford

## Slide 7: CNC turning (1)
All of the processes that can be carried out on a standard lathe can be easily carried out on a CNC lathe.
These include:
– parallel turning
– taper turning
– facing off
– drilling
– parting off.
© Wallingford

## Slide 8: CNC turning (2)
© Wallingford
Some processes, such as turning curved profiles and hemispheres, are very difficult to carry out consistently by hand.
These can be achieved to an extremely high degree of repeatable accuracy using a CNC lathe.
CNC lathes operate on two axes, with the centre line of the billet of material set to zero.
To produce a taper or curved profile, the carriage and top slide stepper motors automatically operate together.

## Slide 9: CNC milling (1)
© Wallingford
All of the processes that can be carried out on a standard vertical milling machine can be easily carried out on a CNC milling machine.
These include:
– facing
– slotting
– grooving.

## Slide 10: CNC milling (2)
© Wallingford
Some processes, such as milling curved profiles and hemispheres, are extremely difficult to carry out by hand.
These can be achieved to a high degree of repeatable accuracy using a CNC milling machine.
The main difference between a standard milling machine and a CNC milling machine is that on a standard machine the cutting tool remains static, and the workpiece is moved towards it along one of three axes, whereas on a CNC milling machine the workpiece remains static, and the cutting tool moves across it along the three axes.

## Slide 11: CNC routing (1)
All of the processes that can be carried out using a hand-held router can be easily carried out on a CNC routing machine.
These include:
– slotting
– grooving
– profiling
– cutting out complex shapes.
© Wallingford

## Slide 12: CNC routing (2)
© Wallingford
The main difference between hand routing and machine routing is that in hand routing the tool is guided around the static workpiece by hand, using the edge or a template as a guide.
In machine routing the workpiece also remains static while the router moves using x, y coordinates to position itself and z coordinates to control the depth of cut.
The process is considerably quicker and more accurate than hand routing; every piece made is exactly to tolerance.

## Slide 13: CNC cutting (1)
© Wallingford
Many of the processes that can be carried out using hand-held cutting tools – knives, and flame torches, plus lasers and water jet – can be carried out using CNC-controlled cutting machines.

## Slide 14: CNC cutting (2)
© Wallingford
Knife cutting is used to cut vinyl, paper and card. It is carried out on either a drum or a flatbed plotter cutter.
Flame cutting uses a plasma cutter on a flat bed to cut metal.
Laser cutting uses a laser on a flat bed to cut and engrave plastic sheet materials such as acrylic and polystyrene, thin timber, cork, leather and glass.
Water cutting uses high-pressure water to cut metal and stone.

## Slide 15: CNC punching (1)
© Wallingford
The advent of CNC has revolutionized the punching of sheet metal, from which products such as filing cabinets and racking systems are manufactured.

## Slide 16: CNC punching (2)
© Wallingford
The sheet material is moved on the bed using CNC x, y coordinates beneath a punching tool.
When it is in position, the tool descends and punches out a piece of material the same shape as the tool.
The end product is either the piece punched out – e.g. a washer – or the sheet of material left, which is then folded to form a cabinet or racking system, for example.

## Slide 17: CNC assembly (1)
© Wallingford
A process that contains repetitive tasks on similar pieces could be suitable for automation.
The number of items of any type to be assembled determines whether or not it is a financially viable proposition to automate a process.

## Slide 18: CNC assembly (2)
If component parts normally need adjustment to fit together correctly, or if they are placed in different positions from one piece to another, it will be difficult, or even impossible, to automate the procedure.
The use of automated assembly lines and cells using robotics works well for repetitive tasks such as the insertion of small components into PCBs, and sub-assemblies of engineering components.
© Wallingford

## Slide 19: CNC welding (1)
© Wallingford
The robots that spot-weld car body panels together look like ballet dancers as they swing in and out of position to perform the next weld.
The robots use 3D modelling to weld the car parts together.
Using 3D mathematical modelling, engineers are able to plan out exactly where the robot needs to make the welds, and how many welds are needed.

## Slide 20: CNC welding (2)
© Wallingford
At the start of a welding cycle the robot swings the welding gun into place.
The welding gun tips squeeze together the two pieces of metal to be welded, with a pressure of around 800kg/m2.
An electrical current is then passed through the tips into the metal that creates a temperature of 1540°C, causing the steel to melt at that point and fuse together.
Each car has thousands of spot welds holding it together.

## Slide 21: CNC painting (1)
© Wallingford
The robots that paint car body panels look like ballet dancers as they swing in and out of position to make the next spray pass.

## Slide 22: CNC painting (2)
© Wallingford
The robots use 3D modelling to paint the car.
Using 3D mathematical modelling, engineers are able to plan out exactly where the robot needs to make the passes required to paint the car, and how many passes are needed to produce an even, high-quality finish.
The spray painting environment is not a pleasant one to work in.
By using robots the risks to the health of employees through the inhalation of toxic fumes are considerably reduced.

## Slide 23: Rapid prototyping (1)
© Wallingford
Rapid prototyping takes virtual CAD designs and transforms them into thin, virtual, horizontal slices.
It then creates each slice in physical space, one after the other, until the model is finished.
The end result of this process is a physical model that exactly matches the virtual model.
Rapid prototyping is an additive fabrication process. It is carried out in the following steps:
– Create a CAD model of the design.
– Convert the CAD model into an STL file.
– Slice the STL file into thin cross-sectional layers.
– Construct the model one layer atop another.
– Clean and finish the model.

## Slide 24: Rapid prototyping (2)
© Wallingford
Rapid prototyping is currently carried out using one of six techniques:
stereolithography
laminated object manufacturing
selective laser sintering
fused deposition modelling
solid ground curing
3D inkjet printing.

## Slide 25: Stereolithography (1)
Stereolithography builds three-dimensional models from liquid photosensitive polymers that solidify when exposed to ultraviolet light.
The model is built on a platform situated just below the surface in a vat of liquid epoxy or acrylate resin.
A low-power, highly focused UV laser traces out the first layer, solidifying the model’s cross-section while leaving excess areas liquid.
© Wallingford

## Slide 26: Stereolithography (2)
An elevator then lowers the platform into the liquid polymer incrementally.
A sweeper re-coats the solidified layer with liquid, and the laser traces the second layer on top of the first.
This process is repeated until the prototype is complete.
Finally the prototype is removed from the vat and rinsed clean of excess liquid.
Supports are broken off, and the model is then placed in an ultraviolet oven for complete curing.
© Wallingford

## Slide 27: Laminated object manufacturing (1)
Laminated object manufacturing is the layering of adhesive-coated sheet material together to form a prototype.
Paper laminated with heat-activated glue and rolled up on spools is fed over the build platform.
A heated roller applies pressure to bond the paper to the base.
© Wallingford

## Slide 28: Laminated object manufacturing (2)
© Wallingford
A focused laser cuts the outline of the first layer into the paper, and then cross-hatches the excess area (the negative space in the prototype).
Cross-hatching breaks up the extra material, making it easier to remove when the prototype is complete.
During the build, the excess material provides excellent support for overhangs and thin-walled sections.
After the first layer is cut, the platform is lowered, and a fresh sheet of material is advanced.

## Slide 29: Laminated object manufacturing (3)
© Wallingford
The platform rises to slightly below the previous height, the roller bonds the second layer to the first, and the laser cuts the second layer.
This process is repeated as needed to build the part, which will have a wood-like texture.
Because the models are made of paper, they must be sealed and finished with paint or varnish to prevent moisture damage.

## Slide 30: Selective laser sintering (1)
© Wallingford
Selective laser sintering uses a laser beam to selectively fuse powdered materials, such as nylon, elastomer or metal, into a solid object.

## Slide 31: Selective laser sintering (2)
Parts are built up on a platform that sits just below the surface in a bin of the heat-fusible powder.
A laser traces the pattern of the first layer, sintering it together.
The platform is lowered by the height of the next layer and powder is reapplied.
This process continues until the part is complete.
Excess powder in each layer helps to support the part during the build.
© Wallingford

## Slide 32: Fused deposit modelling
Fused deposit modelling uses filaments of heated thermoplastic extruded from a tip that moves in the x-y plane to build the prototype.
Rather like a baker decorating a cake, the controlled extrusion head deposits very thin beads of material onto the build platform to form the first layer.
The platform is maintained at a lower temperature, so that the thermoplastic quickly hardens. After the platform lowers, the extrusion head deposits a second layer upon the first.
Supports are built along the way, fastened to the part either with a second, weaker material or with perforated junctions so that they can be easily removed.
© Wallingford

## Slide 33: Solid ground curing (1)
Solid ground curing is rather like stereolithography: both processes use ultraviolet light to selectively harden photosensitive polymers.
First, photosensitive resin is sprayed on the build platform.
Next, the machine prints a mask of the layer to be built on a glass plate above the build platform, using an electrostatic process similar to that used in photocopiers.
The mask is then exposed to UV light, which passes only through the transparent portions of the mask to selectively harden the shape of the current layer.
© Wallingford

## Slide 34: Solid ground curing (2)
© Wallingford
After the layer is cured, the machine vacuums up the excess liquid resin and sprays wax in its place to support the model during the build process.
The top surface is milled flat, and then the process is repeated to build the next layer.
When the part is complete, it has to be de-waxed by immersing it in a solvent bath.
Solid ground curing machines are quite big, and can produce large prototypes.

## Slide 35: 3D inkjet printing (1)
© Wallingford
3D inkjet printing uses machines that employ inkjet technology to produce 3D prototypes.
It is very fast, and produces parts with a slightly grainy surface.
Prototypes are built up on a platform situated in a bin full of powder material.

## Slide 36: 3D inkjet printing (2)
© Wallingford
An inkjet printing head selectively deposits or ‘prints’ a binder fluid to fuse the powder together in the desired areas.
Unbound powder remains to support the part.
The platform is then lowered, more powder is added and levelled, and the process is repeated.
When finished, the completed part is removed from the unbound powder, and excess powder is blown off.
The finished prototype can be sealed to improve durability and surface finish.
Typical layer thicknesses are around 0.1mm.

## Slide 37: Rapid prototyping: advantages and disadvantages (1)
Each of the rapid prototyping systems has its advantages and disadvantages.
The main considerations include
– speed
– the cost of the prototype
– the initial cost of the rapid prototyping machine
– the choice of materials
– colour capabilities.
© Wallingford

## Slide 38: Rapid prototyping: advantages and disadvantages (2)
In laminated object manufacturing, dimensional accuracy is slightly less than that of stereolithography and selected laser sintering, but no milling step is necessary.
Relatively large parts can be made, because no chemical reaction is necessary.
3D printing is optimized for speed, low cost, and ease of use.
This makes it suitable for visualizing during the conceptual stages of the design process, when dimensional accuracy and mechanical strength of the prototypes are of less importance.
© Wallingford

## Slide 39: CAM: advantages and disadvantages
CAM enables repeat jobs to be quickly downloaded and set up.
CAM machines can perform complex tasks with consistent accuracy, so quality is improved.
CAM machines can operate without a rest, so productivity is increased.
CAM machines run on data generated by CAD files that are accurate to a tenth of a millimetre (0.1mm).
CAM machines are expensive to buy.
© Wallingford

## Slide 40: Task: CAM role play (1)
You are one of a team of robots on an automated production line where various tasks are required to be carried out:
Part A has to have four holes drilled in it.
Part B has to have four holes drilled in it.
Part B has to have a thread tapped into the four holes.
The two parts have to be fitted together and four machine screws inserted to hold them together.
© Wallingford

## Slide 41: Task: CAM role play (2)
Four of the assembled parts have to be assembled onto another part by pushing the threaded end through a hole and fitting a washer and nut.
The assembled part is then checked and placed in a crate ready to be transported to the next manufacturing call.
Create an automated CAM production line and role-play the tasks that each robot has to perform in order for the cell to complete the task successfully.
© Wallingford