## Slide 1: Finishing materials
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
© Wallingford
Finishing is the final stage of the manufacturing process.
A well-made product can be ruined by a poor quality finish.
Finishing is carried out for the following reasons:
– to protect the surface of the product in order to prolong its life
– to improve the aesthetic appearance of the product.
There are a wide range of finishes and finishing processes available.
It is important to select the correct one for a particular material and situation.

## Slide 3: Finishing materials
© Wallingford
 | Timber | Metal | Plastic
Painting |  |  | 
Varnishing |  |  | 
Polishing |  |  | 
Staining |  |  | 
Oil |  |  | 
Lacquering |  |  | 
Etching |  |  | 
Anodizing |  |  | 
Electroplating |  |  | 
Galvanizing |  |  | 
Dip coating |  |  | 

## Slide 4: The finishing process
The finishing process begins as soon as the components required to make the product have been manufactured.
As much cleaning up and finishing should be carried out as possible before assembly. This is particularly important on internal surfaces that would be difficult to access after the product has been assembled.
After the surfaces have been cleaned up they need to be prepared.
Timber and metal require different methods of preparation prior to the application of a finish.
Plastics tend not to require any preparation, or the application of a decorative/protective surface finish.
© Wallingford

## Slide 5: Finishing timber (1)
Step 1: Cleaning up
Use a smoothing plane to remove pencil marks and clean the surfaces.
Step 2: Preparation
Use glasspaper to create a smooth surface. This should be done by wrapping the glasspaper around a cork block. Always rub in the same direction as the grain.
Before applying paint to timber, any knots must first be sealed to prevent any resin seeping out, and a coat of primer must be applied.
© Wallingford

## Slide 6: Finishing timber (2)
Step 3: Application of the finish
Liquid finishes should be applied in a warm, dust-free environment.
Liquid finishes should be applied in three or more thin coats, rubbing down lightly between each to build up a deep smooth surface.
When applying a liquid finish with a brush, brush out well and finish with long brushstrokes in the same direction as the grain.
When applying a finish to unassembled components do not apply any to surfaces that are to be glued.
© Wallingford

## Slide 7: Finishes for timber (1)
© Wallingford
Wax polish is made from beeswax dissolved in turpentine to form a paste.
The polish is applied by cloth, and then buffed to give a dull gloss finish that shows off the natural colour and grain of the timber.
Wax polish is suitable for indoor furniture. It is not heat resistant.

## Slide 8: Finishes for timber (2)
© Wallingford
French polish is made by dissolving shellac in methylated spirits.
The first coat is applied using a brush, and subsequent coats are applied by cloth, to build up a high-gloss finish that shows off the natural colour and grain of the timber.
French polish is suitable for indoor furniture.
It is not heat resistant.

## Slide 9: Finishes for timber (3)
Varnish is a solution of natural resins in oil or spirit.
Varnish is applied by brush, spray or cloth and gives a durable, hard, waterproof, high-gloss finish that shows off the natural colour and grain of the timber.
Varnish is used for indoor and outdoor carpentry and furniture.
It is not heat resistant.
© Wallingford

## Slide 10: Finishes for timber (4)
Synthetic varnish is most commonly available as polyurethane. It is a solution of synthetic resins in oil, spirit or water.
Synthetic varnish can be applied by brush, spray or cloth, and gives a very durable, hard, waterproof, high-gloss finish that shows off the natural colour and grain of the timber.
Synthetic varnish is suitable for indoor and outdoor carpentry and furniture.
It is heat resistant.
© Wallingford

## Slide 11: Finishes for timber (5)
© Wallingford
Oil is an especially suitable finish for naturally oily timbers such as teak and iroko.
It can be used on indoor and outdoor furniture, but requires regular re-application in order to maintain protection.
It is applied using a cloth, by rubbing it well into the grain and allowing up to a week between coats.
Olive oil is applied to timber that is to be used with food.

## Slide 12: Finishes for timber (6)
© Wallingford
Stain is used to change the shade or colour of timber.
It is a decorative finish that does not protect the timber; protection is provided by the application of clear varnish when the stain has dried.
Stain can be applied by brush, spray or cloth.

## Slide 13: Finishes for timber (7)
Paint is used to change the colour and protect timber.
When it has been applied, the natural colour and grain pattern are completely obscured.
Paint can be applied by brush or spray, and gives a very durable, hard, waterproof, high-gloss finish.
Paint is suitable for indoor and outdoor carpentry and furniture. It offers some resistance to heat.
Health and safety
Always work in a well-ventilated room when applying finishes, because of the fumes given off. Water-based paints are much safer to use and are more environmentally friendly.
© Wallingford

## Slide 14: Finishing metal (1)
Step 1: Cleaning up
On completion of the shaping processes use drawfiling to remove any marks left.
This is done with a smooth file. Hold the file in both hands, with the hands close to the work, and move the file backwards and forwards.
Use progressively finer grades of emery cloth or wet and dry paper to remove any marks left by drawfiling.
Wrap the abrasive sheet around the file to achieve a flat finish.
© Wallingford

## Slide 15: Finishing metal (2)
Step 2: Preparation
To remove loose scale caused by hot working, use a wire brush and emery cloth.
To clean and degrease the metal use methylated spirit or degreaser to clean badly affected parts.
A solution of caustic soda or detergent will be sufficient to remove light oil and dirt.
Non-ferrous metals can be cleaned and degreased by dipping in a weak acid pickle (one part sulphuric acid to ten parts water).
Always use brass tongs to dip work in a pickle bath, because steel will contaminate the solution.
© Wallingford

## Slide 16: Finishing metal (3)
Step 3: Applying the finish
Liquid finishes should be applied in a warm, dust-free environment.
Liquid finishes should be applied in three or more thin coats, rubbing down lightly between each to build up a deep, smooth surface.
When applying a liquid finish with a brush, brush out well, and finish with long brush strokes along the length of the metal.
© Wallingford

## Slide 17: Finishes for metal (1)
Polishing can done by hand or machine. It is done after all the manufacturing processes have been completed, and before a protective finish is applied.
Polishes contain a very fine abrasive that cuts away the top surface of the metal to create a bright sheen.
Hand polishing is done with a soft cloth and a liquid polish such as Brasso.
Machine polishing is dome with a buffing machine. A polishing compound is applied to a soft mop that revolves at speed; the work is then gently pushed against the mop to polish it.
© Wallingford

## Slide 18: Finishes for metal (2)
Oil can be burnt into the surface of steel to produce an attractive dark blue finish.
The work is heated to a dull red and quenched in oil.
A darker finish can be achieved by using old sump oil.
To protect steel from corrosion, and maintain its bright colour, apply a thin smear of grease over a finished piece of work.
© Wallingford

## Slide 19: Finishes for metal (3)
© Wallingford
Lacquer is usually applied to non-ferrous metals after the final polishing and degreasing has been completed.
Lacquer is similar to varnish, and can be applied by spraying or brush.
The protective coat prevents the metal from coming into contact with air and oxidizing, thereby preserving its polished finish.

## Slide 20: Finishes for metal (4)
© Wallingford
Paint is usually applied to non-ferrous metals after final cleaning up and degreasing, in order to change the colour and protect the metal from oxidization.
Paint is suitable for indoor and outdoor use.
For maximum protection a red oxide paint should be applied, followed by a primer and undercoat before applying the top coat.
Paint can be applied by brush or spray in thin coats to give a very durable, hard, waterproof, high-gloss finish.
Hammerite is a metal paint that does not require the same level of surface preparation, because it can be painted directly onto the metal. It is used mainly on wrought iron work and workshop machinery.

## Slide 21: Finishes for metal (5)
Etching is a decorative finish that produces patterns or designs on the surface of the metal.
The work is first coated with an acid-resist material such as paraffin wax; then the design is created by removing parts of the wax coating to reveal the metal beneath.
The work is then put into an acid bath that etches away the exposed metal: the longer it is in the acid, the deeper the etching.
Finally the acid-resist material is removed to leave a contrasting polished and etched finish.
The work can be lacquered to protect it against oxidization.
© Wallingford

## Slide 22: Finishes for metal (6)
Anodizing is the most common finishing process used on aluminium.
It is used to produce a durable, corrosion-resistant finish, to provide a key for painting and for decoration.
Anodizing is an electrolytic process that thickens the oxide film present on the surface of the metal.
The metal is immersed in a lead-lined bath of chlorine-free electrolyte (sulphuric, chromic and oxalic acids are the most commonly used), and an electric current is passed through. The longer the material is in the bath, the thicker the coating.
Colour can be added to the bath to tint the aluminium.
© Wallingford

## Slide 23: Finishes for metal (7)
Electroplating is used to produce an attractive, durable, corrosion-resistant finish.
Chrome, silver and nickel are some of the most commonly used plating metals.
Electroplating is the depositing of one metal onto another by means of an electric current.
The object to be plated is placed in a bath of metallic salts through which an electric current is passed, causing the salts to dissolve and precipitate onto the object.
© Wallingford

## Slide 24: Finishes for metal (8)
Galvanizing is used to produce a durable, corrosion-resistant finish on steel products that are to be used outside.
Galvanizing is carried out by dipping the finished product into a bath of molten zinc.
© Wallingford

## Slide 25: Finishes for metal (9)
Plastic dip coating is used to produce a durable, corrosion-resistant finish on steel products.
The finished product can be black, white or brightly coloured, depending on the tint added to the powder being used.
Polythene is the most commonly used plastic because of its low cost; nylon and PVC can also be used.
The work is heated to 180°C in an oven.
It is then dipped into a fluidizing tank containing the plastic powder.
It is then returned to the oven to fuse the powder coating into a smooth shiny finish.
If it is left in the oven too long, the plastic will burn.
© Wallingford

## Slide 26: Finishes for plastic
Because plastics do not corrode or decay, there is no need to apply a protective surface coating.
The quality of the moulds used in injection moulding, for instance, mean that there is no further finishing other than the trimming off of any flash or runners and risers.
Finishing acrylic
The cut edges need to be finished by first filing, then drawfiling, followed by wet and dry paper.
Once all of the scratches have been removed, the edges can be polished either by hand, using a cloth and acrylic polish, or on a buffing machine mop to which a suitable acrylic polishing compound has been applied.
© Wallingford

## Slide 27: Tasks
Task 1: Complete the table in Worksheet 1 by adding which finishes are appropriate for use with which materials.
Task 2: Describe with appropriate quality checks the processes that will need to be carried out in order to finish a timber frame project. Use Worksheet 2
© Wallingford