## Slide 1: Joining Materials – Screws, Nuts, Bolts, Nails, Knock-down Fitting, Rivets and Hinges
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Methods of joining materials fall into two broad groups:
Semi-permanent – can be disassembled without damaging the material or the method of joining.
Permanent – cannot be disassembled without damaging the material or the method of joining.
© Wallingford

## Slide 3: Semi-permanent joining methods
 | Timber | Metal | Plastic
Screws |  |  | 
Nuts and bolts |  |  | 
Knock-down fittings |  |  | 
Hinges, catches and stays |  |  | 
© Wallingford

## Slide 4: Woodscrews (1)
Woodscrews provide a neat, strong method of joining timber, and they can be removed easily.
Woodscrews are classified by their length, gauge (diameter), material and type of head.
Woodscrews have a tapering thread that comes to a point.
© Wallingford

## Slide 5: Woodscrews (2)
Woodscrews are most commonly made of steel for cheapness, or brass for appearance and resistance to corrosion.
Steel screws to be used outdoors either galvanized or japanned.
They can also be chrome plated to improve their appearance.
© Wallingford

## Slide 6: Woodscrews (3)
Woodscrews are available in four standard forms:
Countersunk – are the most common; finish flush with the surface; available plated in zinc and nickel.
Round head – usually japanned steel, and used to fix metal fittings outdoors, e.g. hinges, bolts, guttering and downpipes.
Raised countersunk – usually made of chrome-plated steel or brass, and used where appearance is important.
Twinfast – have two threads, which gives them greater holding power in manmade materials such as chipboard, MDF and blockboard.
© Wallingford

## Slide 7: Woodscrews (4)
Woodscrew heads have either straight or crossed screwdriver slots.
Straight slots are the original form, for use with hand screwdrivers.
There is an increased danger of the screwdriver slipping out and damaging the timber when using a powered screwdriver.
Crossed slots were developed as a result of the introduction of powered screwdrivers.
The crossed slot gives a more positive location for the screwdriver tip.
The first was the Phillips, and this has been followed by the Pozidriv and other variations.
© Wallingford

## Slide 8: Using woodscrews
Always screw through the thin piece and into the thick piece.
Drill a pilot hole slightly smaller than the core in the thick piece. Use a bradawl in softwood and a drill in hardwood to make the pilot hole.
Drill a clearance hole in the thin piece, slightly larger than the shank of the screws.
Countersink the clearance hole.
Brass screws can shear off: to avoid this insert a steel screw first, then replace it with a brass one.
© Wallingford

## Slide 9: Self-tapping screws
Self-tapping screws are made from hardened steel, and are able to cut their own thread in sheet metal as they are screwed in.
Using self-tapping screws
Screw through the outer sheet and into the inner sheet.
Drill a pilot hole slightly smaller than the core in the inner sheet. Use a drill to make the pilot hole.
Drill a clearance hole in the outer sheet slightly larger than the shank.
© Wallingford

## Slide 10: Machine screws (1)
Machine screws, also known as set screws, have a parallel thread that goes all the way up to the head.
Machine screws are available in a range of diameters, lengths, heads, materials and threads.
The most common thread form available is ISO metric.
Steel and brass are the most common materials used.
Steel machine screws can also be coated to improve their appearance.
© Wallingford

## Slide 11: Machine screws (2)
© Wallingford
Using machine screws
Drill a tapping size hole equal to the thread root diameter in the inner sheet.
Use a taper tap to cut a thread in the pilot hole. If threading a blind hole, use a bottoming tap to cut the thread to the bottom of the pilot hole,
Drill a clearance hole in the outer sheet slightly larger than the external diameter.

## Slide 12: Nuts and bolts (1)
© Wallingford
Nuts and bolts are used to clamp two pieces of material, usually metal, together. They provide a mechanically strong method of joining materials.
Nuts and bolts are usually made of steel or brass. Steel nuts and bolts can be coated with zinc or chrome to increase resistance to corrosion and improve their appearance.
Bolts are available with hexagonal and square heads; however, hexagonal is the most common.
Bolts have a parallel thread, which can be for all or part of the length. The most common thread form is ISO metric.

## Slide 13: Nuts and bolts (2)
© Wallingford
Bolts are available in in a standard range of lengths up to 150 mm, and diameters up to 25 mm.
Coach bolts are designed for use in timber. They have a shallow domed head with a square underneath, which is designed to bite into the wood to prevent the bolt from turning.
Studding is a long length of headless threaded bar.

## Slide 14: Nuts and bolts (3)
Nuts are screwed onto bolts and provide the clamping force.
They are available most commonly as hexagonal but are also available as square, wing and locking.
Wing nuts are designed to be tightened and undone by hand.
Locking nuts are used to prevent the nut becoming loose due to vibration.
© Wallingford

## Slide 15: Nuts and bolts (4)
Washers are used to spread the load and protect the surface when the nut is tightened.
Spring or lock washers are used to help prevent nuts becoming loosened by vibration.
© Wallingford

## Slide 16: Knock-down fittings (1)
Knock-down (KD) fittings are used extensively in the manufacture of flat-pack furniture.
The advantages of using KD fittings over more traditional joining methods are:
They are ideal for use with manufactured boards such as chipboard and MDF.
They offer increased efficiency and accuracy through the use of drilling jigs.
They reduce the space needed to store completed pieces in the warehouse.
The number of items per load can be increased when transporting.
Customers can fit larger items in their cars and assemble them at home.
© Wallingford

## Slide 17: Knock-down fittings (2)
The most commonly used KD fittings are:
Scan fittings, also known as frame connectors.
They provide a very strong join between the side and end frames without the need to cut joints.
The bolt has a countersunk head with an Allen key socket.
The barrel has a threaded hole through it, and a screwdriver slot with which to align it with the bolt.
© Wallingford

## Slide 18: Knock-down fittings (3)
Cam lock fittings are mainly used in knock-down furniture carcass constructions.
The screw has a extra coarse thread that provides good holding power when inserted into chipboard.
By rotating the cam the two pieces of material are pulled together.
© Wallingford

## Slide 19: Knock-down fittings (4)
Connector block fittings are injection-moulded plastic blocks that provide a simple way to construct carcasses.
They are available as one-piece and two-piece systems.
The two-piece system enables carcasses to be dismantled without the need to remove all the screws.
© Wallingford

## Slide 20: Knock-down fittings (5)
T-nut fittings are threaded inserts with pronged heads that bite into the timber to prevent the fitting spinning as it is tightened.
The ISO metric thread enables it to be used with bolts and machine screws.
© Wallingford

## Slide 21: Knock-down fittings (6)
Threaded inserts have a coarse thread on the outside to enable them to be screwed into chipboard without stripping the material away.
They have an ISO metric threaded hole through the centre into which machine screws and bolts can be screwed.
Corner plate fittings are used to make leg and rail connections on items of furniture such as tables and beds.
As the wing nut is tightened, the leg and rails are brought together.
© Wallingford

## Slide 22: Hinges, locks, catches and stays (1)
Hinges are movable joints that pivot.
They are available in brass, nylon or steel, which can be coated to prevent corrosion and improve appearance.
Butt hinges are used for a wide range of jobs, from small box lids through to hanging doors.
The two leaves of the hinge have to be set into both edges of the wood, and when closed are almost invisible.
© Wallingford

## Slide 23: Hinges, locks, catches and stays (2)
A piano hinge is a long length of butt hinge.
The long length enables the load to be spread.
Back flap hinges are used on drop-down flaps and box lids where strength is required. They are surface fitting, with spaced-out screws for additional strength.
Flush hinges are screwed directly onto the surface, making them easier to fit. One flap fits inside the other when the hinge is closed. They are only suitable for light jobs.
Tee hinges are used in heavy-duty situations such as shed doors and gates. The long flap spreads the load over the pivoting leaf, and the short flap is secured to the static frame.
Pivot hinges are used when you might need to separate a door from its frame. One part is screwed to the door and the other to the frame.
© Wallingford

## Slide 24: Hinges, locks, catches and stays (3)
Locks provide security. There are a vast number of different locks available, each designed to serve a specific purpose. The most commonly used are variations on the following.
Cut cupboard locks are recessed into the edge of a drawer or door to provide a flush finish. They can be fitted horizontally or vertically.
Surface cupboard locks are screwed directly onto the inside surface of a door or drawer, and sit proud.
Box locks are used in situations where a cupboard lock would fall open. A sliding bolt that engages with hooks on the keep prevents it opening.
© Wallingford

## Slide 25: Hinges, locks, catches and stays (4)
Catches provide a means of keeping doors closed without locking them. They are available in brass, nylon or steel, which can be coated to prevent corrosion and improve appearance.
The most commonly used catches are:
Magnetic catches comprise a magnet that is screwed to the carcass and a steel plate that is screwed to the flap.
Ball catches comprise a sprung ball that is screwed to the carcass and a steel plate with a hole in it that is screwed to the flap.
© Wallingford

## Slide 26: Hinges, locks, catches and stays (5)
Spring catches comprise a C-shaped spring that opens as it fits over the catch.
Stays are used to control the opening of horizontally mounted flaps and doors.
When fully opened, the stay is locked at 45° to support the open flap, and it has to be pushed to enable it to close.
© Wallingford

## Slide 27: Permanent joining methods
 | Timber | Metal | Plastic
Adhesives |  |  | 
Nails |  |  | 
Rivets |  |  | 
Box joints |  |  | 
Frame joints |  |  | 
Edge-to-edge joints |  |  | 
Rebates and grooves |  |  | 
Sheet metal joints |  |  | 
Welding |  |  | 
Brazing and soldering |  |  | 
© Wallingford

## Slide 28: Nails (1)
Nailing is a quick way of making a permanent joint in wood.
However, if used on their own, nails produce very weak joints, which only become slightly stronger as the nail rusts inside the timber.
As a nail is hammered in, it punches the fibres away from it.
The fibres then grip the shank of the nail, making it difficult to remove.
Nails cannot easily be removed without damaging the timber.
Nails are sold by type, length, material and weight.
© Wallingford

## Slide 29: Nails (2)
A nail should be approximately three times the length of the thin piece being nailed.
Dovetail nailing – In order to increase the strength of a joint, the nails should be inserted at angles towards each other.
Staggered nailing – In order to avoid splitting the wood when putting in more than one nail, they should be staggered.
© Wallingford

## Slide 30: Nails (3)
Round wire nails are used for general joinery work.
They have round shanks and a flat head, and are made from steel, which can be galvanized to prevent rusting.
They range from 12mm to 150mm in length.
Oval wire nails are used for general joinery work.
They have oval shanks and a narrow head, which is driven below the surface to provide a flush finish.
The long axis of the oval shank is lined up with the grain direction to reduce the risk of splitting.
They range from 12mm to 150mm in length.
© Wallingford

## Slide 31: Nails (4)
Annular ring nails have greater holding power than other types of nail.
They have ridged rings along their length that bite into the wood, making them very difficult to pull out.
They range from 20mm to 75mm in length.
Panel pins are used for strengthening joints and fixing sheet materials.
They have thin round shanks and a small head, which is driven below the surface with a nail punch to provide a flush finish.
They range from 12mm to 50mm in length.
Hardboard pins have a hard square shank, which can penetrate hardboard without bending.
The pointed head does not need to be punched below the surface.
© Wallingford

## Slide 32: Rivets (1)
Rivets are predominantly used to make permanent joints in sheet metal, but the process can also be used to join acrylic, plywood and other soft materials together and to each other.
Rivets work by forming a head on both sides of the material being joined.
There are two different types of rivet:
– solid rivets
– blind rivets, also known as pop rivets.
© Wallingford

## Slide 33: Rivets (2)
Solid rivets are made of either soft mild steel, aluminium or copper. They are available with countersunk, flat, or round heads.
Countersunk head rivets are the most commonly used, and produce a flush finish.
Round head rivets are used where a flush finish is not required, or where countersinking would weaken the material.
Flat head rivets are used to join thin sheet material where countersinking would not be possible.
© Wallingford

## Slide 34: Rivets (3)
How to install a countersink rivet:
Drill holes in both pieces of material the same diameter as the shank of the rivet, and de-burr.
Countersink the outer surface of both pieces of material to the depth of the rivet head.
Cut the rivet so that an amount equivalent to the diameter is sticking up.
Assemble the joint and place on a metal block.
Swell the rivet in the hole by striking with the flat face of a ball pein hammer.
Use the ball pein to hammer the rivet into the countersink.
File smooth.
© Wallingford

## Slide 35: Rivets (4)
Blind rivets are more commonly known as pop rivets. The main advantage over solid rivets is that they are quicker to install, and can be installed from one side only.
Blind rivets are weaker than solid rivets because they are hollow, and made from softer material.
They are used to join thin sheet metal, but they can also be used with other thin materials.
The rivet is inserted into a rivet gun and pushed through both pieces of material.
As the gun is pressed the mandrel is pulled back, causing the rivet to swell.
When the correct pressure is reached the mandrel breaks off to leave the rivet in place.
© Wallingford