## Slide 1: Joining Materials - Metal
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Methods of joining materials fall into two broad groups:
Semi-permanent – can be disassembled without damaging the material or the method of joining.
Permanent – cannot be disassembled without damaging the material or the method of joining.
© Wallingford

## Slide 3: Permanent joining methods
 | Timber | Metal | Plastic
Adhesives |  |  | 
Nails |  |  | 
Rivets |  |  | 
Box joints |  |  | 
Frame joints |  |  | 
Edge-to-edge joints |  |  | 
Rebates and grooves |  |  | 
Sheet metal joints |  |  | 
Welding |  |  | 
Brazing and soldering |  |  | 
© Wallingford

## Slide 4: Joints in metal
Frame joints – When fabricating frame constructions in metal, many of the same joints as those used when working with timber are used.
This is in order to increase the area of contact when the joint is made by welding, brazing or soldering.
Sheet metal joints – Edge-to-edge joints such as butt joints are not suitable for joining thin sheet metal.
In order to increase the surface area for joining, special joints are used, some of which also provide a mechanical connection.
© Wallingford

## Slide 5: Welding, brazing and soldering
Welding, brazing and soldering are all heat-based processes used to make permanent joints in metal.
Process | Filler rod | Flux | Melting point
Welding | Same as metal | None needed for steel | Same as metal
Brazing | 65% Copper, 35% zinc | Borax | 875°C
Silver soldering (copper and zinc plus silver) | Enamelling = 81% silver | Borax | 800°C
 | Hard = 78% silver | Borax | 775°C
 | Medium = 74% silver | Borax | 750°C
 | Easy = 67% silver | Borax | 720°C
 | Easy-flo = 50% silver | Easy-flo | 625°C
Soft soldering | Lead, tin and antimony | Zinc chloride | 200°C
© Wallingford

## Slide 6: Welding (1)
Welding is a process that melts the surfaces of the two pieces of material being joined, and fuses them together.
This makes the join as strong as the original material.
Although welding is most commonly associated with the joining of metals, it can also used to join some plastics.
The different types of welding are:
– oxyacetylene gas
– MIG (metal inert gas)
– TIG (tungsten electrode inert gas)
– spot.
© Wallingford

## Slide 7: Welding (2)
Gas welding uses a torch to heat up the metals being joined.
A mixture of acetylene and oxygen is fed from separate tanks through the torch to produce a small but very hot flame.
When the metal reaches the right temperature, a filler rod of metal is applied to the joint to make the weld.
© Wallingford

## Slide 8: Welding (3)
MIG welding (metal inert gas) is an electric arc welding process.
An electric arc is struck between the material being welded and a continuous wire electrode, which is fed through a torch.
An inert gas, argon, flows though the torch to provide a shield around the arc to prevent the surface oxidizing.
The continuous wire rod provides the filler rod.
© Wallingford

## Slide 9: Welding (4)
TIG welding (tungsten electrode inert gas) is an electric arc welding process, very similar to MIG welding.
An electric arc is struck between the material being welded and a tungsten electrode, which is fed through a torch.
An inert gas, argon, flows though the torch to provide a shield around the arc to prevent the surface oxidizing.
TIG welding is particularly suited to welding aluminium and stainless steel.
© Wallingford

## Slide 10: Welding (5)
Spot welding is a form of resistance welding, and is used for joining thin sheet steel together, e.g. car door panels.
Two copper electrodes are clamped to the metal at the point where the join is to be made, and an electric current is passed between them.
At the point where there is most resistance to the current flow, heat is generated, and this is the point at which the weld is made.
Spot welding is often carried out by robots that have been programmed to make the series of welds necessary to weld two panels together.
© Wallingford

## Slide 11: Brazing and silver soldering (1)
Brazing is a method of joining metal with a melted solder called brazing spelter.
This is a mixture of copper and zinc that melts at around 875°C. Its high melting point makes it most suitable for use with ferrous metals.
Silver soldering or hard soldering is a method of joining metal with a melted solder called silver solder.
This is a mixture of copper, zinc and silver that, depending on the ratio, melts at different temperatures, from 625°C to 800°C.
By using a range of solders with progressively lower melting points it is possible to make several joins in sequential stages.
© Wallingford

## Slide 12: Brazing and silver soldering (2)
How to make a brazed or silver soldered joint
Make sure the surfaces to be joined are a good fit, and clean.
If necessary, wire them together to prevent movement.
Place on the brazing hearth, surrounded by firebricks.
Apply a suitable flux to keep the joint clean.
Warm up the joint with a ‘fluffy’ flame.
Heat up the joint to red heat with a strong flame.
Apply solder to the join line until it flows and the joint is made.
Allow to cool.
© Wallingford

## Slide 13: Soft soldering
Soft soldering is a quick and easy method of joining copper, brass and tinplate. It is also used to connect electronic components to printed circuit boards.
Soft solder is an alloy of lead, tin and antimony. The joining process relies on alloying: the tin alloys with the surface of the metal being joined.
Soft solders used for electronics contain more lead than those used for sheet metalwork and plumbing. This makes them flow more easily, but the finished joint is not as hard.
© Wallingford

## Slide 14: Welding plastics
The process is basically the same as welding metals, in that the two surfaces to be joined are heated until they soften, and pressure applied to make the weld. Only thermoplastics that do not burn when heated to their melting point can be welded.
The two methods most commonly used are:
Hot air – The seam to be joined is heated using hot air and a filler rod of the same material is applied as the nozzle moves along.
Heated tool – A heated tool similar to a soldering iron is passed over the join, causing the material to melt and fuse.
© Wallingford