## Slide 1: Joining Materials
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Methods of joining materials fall into two broad groups:
Semi-permanent – can be disassembled without damaging the material or the method of joining.
Permanent – cannot be disassembled without damaging the material or the method of joining.
© Wallingford

## Slide 3: Starter
How many different methods of joining materials can you name?
© Wallingford

## Slide 4: Semi-permanent joining methods
 | Timber | Metal | Plastic
Screws |  |  | 
Nuts and bolts |  |  | 
Knock-down fittings |  |  | 
Hinges, catches and stays |  |  | 
© Wallingford

## Slide 5: Woodscrews (1)
Woodscrews provide a neat, strong method of joining timber, and they can be removed easily.
Woodscrews are classified by their length, gauge (diameter), material and type of head.
Woodscrews have a tapering thread that comes to a point.
© Wallingford

## Slide 6: Woodscrews (2)
Woodscrews are most commonly made of steel for cheapness, or brass for appearance and resistance to corrosion.
Steel screws to be used outdoors either galvanized or japanned.
They can also be chrome plated to improve their appearance.
© Wallingford

## Slide 7: Woodscrews (3)
Woodscrews are available in four standard forms:
Countersunk – are the most common; finish flush with the surface; available plated in zinc and nickel.
Round head – usually japanned steel, and used to fix metal fittings outdoors, e.g. hinges, bolts, guttering and downpipes.
Raised countersunk – usually made of chrome-plated steel or brass, and used where appearance is important.
Twinfast – have two threads, which gives them greater holding power in manmade materials such as chipboard, MDF and blockboard.
© Wallingford

## Slide 8: Woodscrews (4)
Woodscrew heads have either straight or crossed screwdriver slots.
Straight slots are the original form, for use with hand screwdrivers.
There is an increased danger of the screwdriver slipping out and damaging the timber when using a powered screwdriver.
Crossed slots were developed as a result of the introduction of powered screwdrivers.
The crossed slot gives a more positive location for the screwdriver tip.
The first was the Phillips, and this has been followed by the Pozidriv and other variations.
© Wallingford

## Slide 9: Using woodscrews
Always screw through the thin piece and into the thick piece.
Drill a pilot hole slightly smaller than the core in the thick piece. Use a bradawl in softwood and a drill in hardwood to make the pilot hole.
Drill a clearance hole in the thin piece, slightly larger than the shank of the screws.
Countersink the clearance hole.
Brass screws can shear off: to avoid this insert a steel screw first, then replace it with a brass one.
© Wallingford

## Slide 10: Self-tapping screws
Self-tapping screws are made from hardened steel, and are able to cut their own thread in sheet metal as they are screwed in.
Using self-tapping screws
Screw through the outer sheet and into the inner sheet.
Drill a pilot hole slightly smaller than the core in the inner sheet. Use a drill to make the pilot hole.
Drill a clearance hole in the outer sheet slightly larger than the shank.
© Wallingford

## Slide 11: Machine screws (1)
Machine screws, also known as set screws, have a parallel thread that goes all the way up to the head.
Machine screws are available in a range of diameters, lengths, heads, materials and threads.
The most common thread form available is ISO metric.
Steel and brass are the most common materials used.
Steel machine screws can also be coated to improve their appearance.
© Wallingford

## Slide 12: Machine screws (2)
© Wallingford
Using machine screws
Drill a tapping size hole equal to the thread root diameter in the inner sheet.
Use a taper tap to cut a thread in the pilot hole. If threading a blind hole, use a bottoming tap to cut the thread to the bottom of the pilot hole,
Drill a clearance hole in the outer sheet slightly larger than the external diameter.

## Slide 13: Nuts and bolts (1)
© Wallingford
Nuts and bolts are used to clamp two pieces of material, usually metal, together. They provide a mechanically strong method of joining materials.
Nuts and bolts are usually made of steel or brass. Steel nuts and bolts can be coated with zinc or chrome to increase resistance to corrosion and improve their appearance.
Bolts are available with hexagonal and square heads; however, hexagonal is the most common.
Bolts have a parallel thread, which can be for all or part of the length. The most common thread form is ISO metric.

## Slide 14: Nuts and bolts (2)
© Wallingford
Bolts are available in in a standard range of lengths up to 150 mm, and diameters up to 25 mm.
Coach bolts are designed for use in timber. They have a shallow domed head with a square underneath, which is designed to bite into the wood to prevent the bolt from turning.
Studding is a long length of headless threaded bar.

## Slide 15: Nuts and bolts (3)
Nuts are screwed onto bolts and provide the clamping force.
They are available most commonly as hexagonal but are also available as square, wing and locking.
Wing nuts are designed to be tightened and undone by hand.
Locking nuts are used to prevent the nut becoming loose due to vibration.
© Wallingford

## Slide 16: Nuts and bolts (4)
Washers are used to spread the load and protect the surface when the nut is tightened.
Spring or lock washers are used to help prevent nuts becoming loosened by vibration.
© Wallingford

## Slide 17: Knock-down fittings (1)
Knock-down (KD) fittings are used extensively in the manufacture of flat-pack furniture.
The advantages of using KD fittings over more traditional joining methods are:
They are ideal for use with manufactured boards such as chipboard and MDF.
They offer increased efficiency and accuracy through the use of drilling jigs.
They reduce the space needed to store completed pieces in the warehouse.
The number of items per load can be increased when transporting.
Customers can fit larger items in their cars and assemble them at home.
© Wallingford

## Slide 18: Knock-down fittings (2)
The most commonly used KD fittings are:
Scan fittings, also known as frame connectors.
They provide a very strong join between the side and end frames without the need to cut joints.
The bolt has a countersunk head with an Allen key socket.
The barrel has a threaded hole through it, and a screwdriver slot with which to align it with the bolt.
© Wallingford

## Slide 19: Knock-down fittings (3)
Cam lock fittings are mainly used in knock-down furniture carcass constructions.
The screw has a extra coarse thread that provides good holding power when inserted into chipboard.
By rotating the cam the two pieces of material are pulled together.
© Wallingford

## Slide 20: Knock-down fittings (4)
Connector block fittings are injection-moulded plastic blocks that provide a simple way to construct carcasses.
They are available as one-piece and two-piece systems.
The two-piece system enables carcasses to be dismantled without the need to remove all the screws.
© Wallingford

## Slide 21: Knock-down fittings (5)
T-nut fittings are threaded inserts with pronged heads that bite into the timber to prevent the fitting spinning as it is tightened.
The ISO metric thread enables it to be used with bolts and machine screws.
© Wallingford

## Slide 22: Knock-down fittings (6)
Threaded inserts have a coarse thread on the outside to enable them to be screwed into chipboard without stripping the material away.
They have an ISO metric threaded hole through the centre into which machine screws and bolts can be screwed.
Corner plate fittings are used to make leg and rail connections on items of furniture such as tables and beds.
As the wing nut is tightened, the leg and rails are brought together.
© Wallingford

## Slide 23: Hinges, locks, catches and stays (1)
Hinges are movable joints that pivot.
They are available in brass, nylon or steel, which can be coated to prevent corrosion and improve appearance.
Butt hinges are used for a wide range of jobs, from small box lids through to hanging doors.
The two leaves of the hinge have to be set into both edges of the wood, and when closed are almost invisible.
© Wallingford

## Slide 24: Hinges, locks, catches and stays (2)
A piano hinge is a long length of butt hinge.
The long length enables the load to be spread.
Back flap hinges are used on drop-down flaps and box lids where strength is required. They are surface fitting, with spaced-out screws for additional strength.
Flush hinges are screwed directly onto the surface, making them easier to fit. One flap fits inside the other when the hinge is closed. They are only suitable for light jobs.
Tee hinges are used in heavy-duty situations such as shed doors and gates. The long flap spreads the load over the pivoting leaf, and the short flap is secured to the static frame.
Pivot hinges are used when you might need to separate a door from its frame. One part is screwed to the door and the other to the frame.
© Wallingford

## Slide 25: Hinges, locks, catches and stays (3)
Locks provide security. There are a vast number of different locks available, each designed to serve a specific purpose. The most commonly used are variations on the following.
Cut cupboard locks are recessed into the edge of a drawer or door to provide a flush finish. They can be fitted horizontally or vertically.
Surface cupboard locks are screwed directly onto the inside surface of a door or drawer, and sit proud.
Box locks are used in situations where a cupboard lock would fall open. A sliding bolt that engages with hooks on the keep prevents it opening.
© Wallingford

## Slide 26: Hinges, locks, catches and stays (4)
Catches provide a means of keeping doors closed without locking them. They are available in brass, nylon or steel, which can be coated to prevent corrosion and improve appearance.
The most commonly used catches are:
Magnetic catches comprise a magnet that is screwed to the carcass and a steel plate that is screwed to the flap.
Ball catches comprise a sprung ball that is screwed to the carcass and a steel plate with a hole in it that is screwed to the flap.
© Wallingford

## Slide 27: Hinges, locks, catches and stays (5)
Spring catches comprise a C-shaped spring that opens as it fits over the catch.
Stays are used to control the opening of horizontally mounted flaps and doors.
When fully opened, the stay is locked at 45° to support the open flap, and it has to be pushed to enable it to close.
© Wallingford

## Slide 28: Permanent joining methods
 | Timber | Metal | Plastic
Adhesives |  |  | 
Nails |  |  | 
Rivets |  |  | 
Box joints |  |  | 
Frame joints |  |  | 
Edge-to-edge joints |  |  | 
Rebates and grooves |  |  | 
Sheet metal joints |  |  | 
Welding |  |  | 
Brazing and soldering |  |  | 
© Wallingford

## Slide 29: Adhesives (1)
All joints that are made using adhesives are permanent.
There are many different types of adhesive for use on different materials and in different situations.
Adhesives will work only if the correct one for the job is used, and if the surfaces to be joined are clean, free from dust and grease.
Health and safety
Many adhesives give off toxic fumes and should only be used in well-ventilated areas.
© Wallingford

## Slide 30: Adhesives (2)
The table below shows which adhesives should be used with which material.
 | Timber | Metal | Plastic | Fabric
Timber | PVA or synthetic | Contact adhesive | Contact adhesive | PVA
Metal | Contact adhesive | Epoxy resin | Contact adhesive | Contact adhesive
Plastic | Contact adhesive | Epoxy Resin | Solvent cement | Contact adhesive
Fabric | PVA | Contact adhesive | Contact adhesive | Latex
© Wallingford

## Slide 31: Adhesives (3)
PVA (polyvinyl acetate) is the most commonly used wood glue.
It is a water-based adhesive, and works by soaking into the surface of the timber and setting when the water has been absorbed.
It is supplied in liquid form, ready to use; it is easy to apply, non-staining, and produces a strong bond.
Exterior-grade PVA must be used if there is a risk of the joint getting wet.
© Wallingford

## Slide 32: Adhesives (4)
Synthetic resin (Cascamite) is a stronger wood glue than PVA, and is also waterproof.
It is supplied in powder form, and has to be mixed with water.
When it has cured it forms a very strong, hard, brittle bond.
© Wallingford

## Slide 33: Adhesives (5)
Epoxy resin (e.g. Araldite) is an expensive adhesive that could be used to stick almost any clean and dry materials to each other.
However, because of the high cost it tends to be used for special purposes.
A resin and hardener are mixed together in equal amounts, and hardening begins immediately.
The adhesive is fully cured after several hours.
It makes an extremely strong and hard bond.
© Wallingford

## Slide 34: Adhesives (6)
Solvent cement (e.g. Tensol) works by dissolving the hard surface of hard plastics such as acrylic and high-impact polystyrene.
© Wallingford

## Slide 35: Adhesives (7)
Contact adhesive (e.g. Evostik) is used for gluing sheet materials such as melamine to work surfaces.
It works by applying it to both surfaces and allowing them to become touch dry.
Adhesion takes place as soon as the two surfaces make contact and there is no opportunity for repositioning – so get it right first time or else!
© Wallingford

## Slide 36: Adhesives (8)
Latex (e.g. Copydex) is used to bond paper, card and fabrics.
Hot-melt glue is applied using a glue gun, which melts the glue stick.
It is useful for modelling, but is of limited use otherwise.
© Wallingford

## Slide 37: Nails (1)
Nailing is a quick way of making a permanent joint in wood.
However, if used on their own, nails produce very weak joints, which only become slightly stronger as the nail rusts inside the timber.
As a nail is hammered in, it punches the fibres away from it.
The fibres then grip the shank of the nail, making it difficult to remove.
Nails cannot easily be removed without damaging the timber.
Nails are sold by type, length, material and weight.
© Wallingford

## Slide 38: Nails (2)
A nail should be approximately three times the length of the thin piece being nailed.
Dovetail nailing – In order to increase the strength of a joint, the nails should be inserted at angles towards each other.
Staggered nailing – In order to avoid splitting the wood when putting in more than one nail, they should be staggered.
© Wallingford

## Slide 39: Nails (3)
Round wire nails are used for general joinery work.
They have round shanks and a flat head, and are made from steel, which can be galvanized to prevent rusting.
They range from 12mm to 150mm in length.
Oval wire nails are used for general joinery work.
They have oval shanks and a narrow head, which is driven below the surface to provide a flush finish.
The long axis of the oval shank is lined up with the grain direction to reduce the risk of splitting.
They range from 12mm to 150mm in length.
© Wallingford

## Slide 40: Nails (4)
Annular ring nails have greater holding power than other types of nail.
They have ridged rings along their length that bite into the wood, making them very difficult to pull out.
They range from 20mm to 75mm in length.
Panel pins are used for strengthening joints and fixing sheet materials.
They have thin round shanks and a small head, which is driven below the surface with a nail punch to provide a flush finish.
They range from 12mm to 50mm in length.
Hardboard pins have a hard square shank, which can penetrate hardboard without bending.
The pointed head does not need to be punched below the surface.
© Wallingford

## Slide 41: Rivets (1)
Rivets are predominantly used to make permanent joints in sheet metal, but the process can also be used to join acrylic, plywood and other soft materials together and to each other.
Rivets work by forming a head on both sides of the material being joined.
There are two different types of rivet:
– solid rivets
– blind rivets, also known as pop rivets.
© Wallingford

## Slide 42: Rivets (2)
Solid rivets are made of either soft mild steel, aluminium or copper. They are available with countersunk, flat, or round heads.
Countersunk head rivets are the most commonly used, and produce a flush finish.
Round head rivets are used where a flush finish is not required, or where countersinking would weaken the material.
Flat head rivets are used to join thin sheet material where countersinking would not be possible.
© Wallingford

## Slide 43: Rivets (3)
How to install a countersink rivet:
Drill holes in both pieces of material the same diameter as the shank of the rivet, and de-burr.
Countersink the outer surface of both pieces of material to the depth of the rivet head.
Cut the rivet so that an amount equivalent to the diameter is sticking up.
Assemble the joint and place on a metal block.
Swell the rivet in the hole by striking with the flat face of a ball pein hammer.
Use the ball pein to hammer the rivet into the countersink.
File smooth.
© Wallingford

## Slide 44: Rivets (4)
Blind rivets are more commonly known as pop rivets. The main advantage over solid rivets is that they are quicker to install, and can be installed from one side only.
Blind rivets are weaker than solid rivets because they are hollow, and made from softer material.
They are used to join thin sheet metal, but they can also be used with other thin materials.
The rivet is inserted into a rivet gun and pushed through both pieces of material.
As the gun is pressed the mandrel is pulled back, causing the rivet to swell.
When the correct pressure is reached the mandrel breaks off to leave the rivet in place.
© Wallingford

## Slide 45: Box joints (1)
Box joints are used to construct carcasses. Carcass constructions include cupboards, drawers and bookcases.
Examples of box joints include:
butt joint (A, B, C, D)
corner rebate joint (A)
finger or comb joint (A)
dovetail joint (A)
dowel joint (A, B, C, D)
biscuit joint (A, B, C, D)
housing joint (A, B, C, D).
© Wallingford

## Slide 46: Box joints (2)
Butt joint – is the simplest and quickest to construct; however, it is not very strong.
It can be reinforced by dovetail nailing and corner blocks.
Corner rebate or lap joint – is stronger than a butt joint, because of the increased gluing area; however, it is still not very strong.
It can be reinforced by dovetail nailing.
© Wallingford

## Slide 47: Box joints (3)
Finger or comb joint – is stronger than a butt joint because of the mechanical connection and the increased gluing area.
Finger joints were developed by the furniture industry as a more efficient method of mass production.
Dovetail joint – is the strongest carcass joint, thanks to the complex mechanical connection and the significantly increased gluing area.
Dovetail joints can only be assembled in one direction, and can therefore only be pulled apart in one direction, making them particularly good when constructing drawers.
© Wallingford

## Slide 48: Box joints (4)
Dowel joint – is suitable for both corner and tee joints.
It is a particularly useful joint when working with chipboard and MDF.
Dowels are often combined with KD fittings such as cam locks in flat-pack furniture.
© Wallingford

## Slide 49: Box joints (5)
Biscuit joint – is used to join manmade boards.
A biscuit jointer cuts slots in both halves to be joined, into which an elliptical-shaped biscuit is inserted to make a mechanical connection.
The biscuits are elliptical pieces of timber that have been dried and compressed.
Once the glue is applied, the biscuit swells and reinforces the joint.
Biscuit joints are used extensively in commercial furniture manufacture.
© Wallingford

## Slide 50: Box joints (6)
Housing joint – is used to secure shelves and partitions in carcass constructions.
A through housing is the simplest to construct.
If it is desirable that the joint does not show, a stopped housing can be used.
If there is a danger of the joint being pulled apart, the dovetail housing provides additional lateral strength. They can be through or stopped.
© Wallingford

## Slide 51: Frame joints (1)
Frame joints fall into two broad groups: flat frame joints and three-dimensional frame joints.
Flat frame joints are used to construct picture frames, door frames and window frames.
Joints used in the manufacture of flat frames include:
– butt joint (A, B, C)
– mitre joint (D)
– halving joint (A, B, C)
– bridle joint (A, B )
– mortise and tenon joint (A, B, C)
– dowel joint (A, B, C).
© Wallingford

## Slide 52: Frame joints (2)
Three-dimensional frame joints are used to construct tables, chairs, beds and buildings where three or more pieces of timber meet.
Joints used in the manufacture of three-dimensional frames include:
– halving joints (C)
– bridle joints (C)
– mortise and tenon joints (A, B, C)
– dowel joints (A, B, C).
© Wallingford

## Slide 53: Frame joints (3)
Butt joint – is the simplest and quickest to construct; however, it is not very strong. It can be reinforced by dovetail nailing and corner blocks.
Mitre joint – is made by cutting both pieces to be joined at the same angle – 45° for a square or rectangular frame.
No end grain is shown.
The mitre can be reinforced by nailing, or by the insertion of veneer keys into saw cuts made across the joint.
© Wallingford

## Slide 54: Frame joints (4)
Halving joints – are stronger than butt joints, thanks to the increased gluing area.
They can be reinforced by dovetail nailing, screwing or dowelling.
Halving joints are made by removing half of the material thickness from both pieces at the point where they intersect.
Halving joints can be used to make corner, tee and cross joins.
© Wallingford

## Slide 55: Frame joints (5)
Bridle joints – are stronger than halving joints, thanks to the increased gluing area.
They can be reinforced by dovetail nailing, screwing or dowelling.
Bridle joints are made by removing the material thickness in thirds from both pieces at the point where they intersect.
Bridle joints can be used to make corner and tee joins.
© Wallingford

## Slide 56: Frame joints (6)
Dowel joints – are butt joints reinforced with dowel pegs.
They are strong, thanks to the mechanical connection and the increased gluing area.
Dowel joints are made by drilling holes equal to the diameter of the dowel being used in both pieces of material, at the point where they intersect.
If several joints are to be made, it is advisable to use a jig to speed up the process and ensure the holes line up.
Dowel joints can be used to make corner and tee joins.
© Wallingford

## Slide 57: Frame joints (7)
Mortise and tenon joints – are stronger than halving joints, thanks to the increased gluing area.
They can be reinforced by dowelling or, in the case of a through mortise, it can be wedged.
Mortise and tenon joints are made by removing the material thickness in thirds from both pieces at the point where they intersect.
Mortise and tenon joints can be used to make corner and tee joins.
When the joint is to be made at the end of a piece of timber, a haunched joint is used.
The sloping haunch is not visible when it is glued together.
© Wallingford

## Slide 58: Edge-to-edge joints
Edge-to-edge joints – are used to join planks of natural timber edge to edge, and to add a more attractive lipping to the edge of manmade boards.
When joining natural timber boards edge to edge, the edges must be planed true.
By alternating the curve displayed on the end grain, the distortion caused by cupping is reduced.
© Wallingford

## Slide 59: Rebates and grooves
Rebates are used to insert the backs of cupboards, lids and bases into boxes, glass and decorative panels.
Grooves are used to insert the backs of cupboards, lids and bases into boxes, glass and decorative panels.
They can also be used to create sliding panels by using two grooves.
Grooves provide a more secure method of fixing than rebates.
© Wallingford

## Slide 60: Joints in metal
Frame joints – When fabricating frame constructions in metal, many of the same joints as those used when working with timber are used.
This is in order to increase the area of contact when the joint is made by welding, brazing or soldering.
Sheet metal joints – Edge-to-edge joints such as butt joints are not suitable for joining thin sheet metal.
In order to increase the surface area for joining, special joints are used, some of which also provide a mechanical connection.
© Wallingford

## Slide 61: Welding, brazing and soldering
Welding, brazing and soldering are all heat-based processes used to make permanent joints in metal.
Process | Filler rod | Flux | Melting point
Welding | Same as metal | None needed for steel | Same as metal
Brazing | 65% Copper, 35% zinc | Borax | 875°C
Silver soldering (copper and zinc plus silver) | Enamelling = 81% silver | Borax | 800°C
 | Hard = 78% silver | Borax | 775°C
 | Medium = 74% silver | Borax | 750°C
 | Easy = 67% silver | Borax | 720°C
 | Easy-flo = 50% silver | Easy-flo | 625°C
Soft soldering | Lead, tin and antimony | Zinc chloride | 200°C
© Wallingford

## Slide 62: Welding (1)
Welding is a process that melts the surfaces of the two pieces of material being joined, and fuses them together.
This makes the join as strong as the original material.
Although welding is most commonly associated with the joining of metals, it can also used to join some plastics.
The different types of welding are:
– oxyacetylene gas
– MIG (metal inert gas)
– TIG (tungsten electrode inert gas)
– spot.
© Wallingford

## Slide 63: Welding (2)
Gas welding uses a torch to heat up the metals being joined.
A mixture of acetylene and oxygen is fed from separate tanks through the torch to produce a small but very hot flame.
When the metal reaches the right temperature, a filler rod of metal is applied to the joint to make the weld.
© Wallingford

## Slide 64: Welding (3)
MIG welding (metal inert gas) is an electric arc welding process.
An electric arc is struck between the material being welded and a continuous wire electrode, which is fed through a torch.
An inert gas, argon, flows though the torch to provide a shield around the arc to prevent the surface oxidizing.
The continuous wire rod provides the filler rod.
© Wallingford

## Slide 65: Welding (4)
TIG welding (tungsten electrode inert gas) is an electric arc welding process, very similar to MIG welding.
An electric arc is struck between the material being welded and a tungsten electrode, which is fed through a torch.
An inert gas, argon, flows though the torch to provide a shield around the arc to prevent the surface oxidizing.
TIG welding is particularly suited to welding aluminium and stainless steel.
© Wallingford

## Slide 66: Welding (5)
Spot welding is a form of resistance welding, and is used for joining thin sheet steel together, e.g. car door panels.
Two copper electrodes are clamped to the metal at the point where the join is to be made, and an electric current is passed between them.
At the point where there is most resistance to the current flow, heat is generated, and this is the point at which the weld is made.
Spot welding is often carried out by robots that have been programmed to make the series of welds necessary to weld two panels together.
© Wallingford

## Slide 67: Brazing and silver soldering (1)
Brazing is a method of joining metal with a melted solder called brazing spelter.
This is a mixture of copper and zinc that melts at around 875°C. Its high melting point makes it most suitable for use with ferrous metals.
Silver soldering or hard soldering is a method of joining metal with a melted solder called silver solder.
This is a mixture of copper, zinc and silver that, depending on the ratio, melts at different temperatures, from 625°C to 800°C.
By using a range of solders with progressively lower melting points it is possible to make several joins in sequential stages.
© Wallingford

## Slide 68: Brazing and silver soldering (2)
How to make a brazed or silver soldered joint
Make sure the surfaces to be joined are a good fit, and clean.
If necessary, wire them together to prevent movement.
Place on the brazing hearth, surrounded by firebricks.
Apply a suitable flux to keep the joint clean.
Warm up the joint with a ‘fluffy’ flame.
Heat up the joint to red heat with a strong flame.
Apply solder to the join line until it flows and the joint is made.
Allow to cool.
© Wallingford

## Slide 69: Soft soldering
Soft soldering is a quick and easy method of joining copper, brass and tinplate. It is also used to connect electronic components to printed circuit boards.
Soft solder is an alloy of lead, tin and antimony. The joining process relies on alloying: the tin alloys with the surface of the metal being joined.
Soft solders used for electronics contain more lead than those used for sheet metalwork and plumbing. This makes them flow more easily, but the finished joint is not as hard.
© Wallingford

## Slide 70: Welding plastics
The process is basically the same as welding metals, in that the two surfaces to be joined are heated until they soften, and pressure applied to make the weld. Only thermoplastics that do not burn when heated to their melting point can be welded.
The two methods most commonly used are:
Hot air – The seam to be joined is heated using hot air and a filler rod of the same material is applied as the nozzle moves along.
Heated tool – A heated tool similar to a soldering iron is passed over the join, causing the material to melt and fuse.
© Wallingford