## Slide 1: Joining Materials - Wood
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Methods of joining materials fall into two broad groups:
Semi-permanent – can be disassembled without damaging the material or the method of joining.
Permanent – cannot be disassembled without damaging the material or the method of joining.
© Wallingford

## Slide 3: Permanent joining methods
 | Timber | Metal | Plastic
Adhesives |  |  | 
Nails |  |  | 
Rivets |  |  | 
Box joints |  |  | 
Frame joints |  |  | 
Edge-to-edge joints |  |  | 
Rebates and grooves |  |  | 
Sheet metal joints |  |  | 
Welding |  |  | 
Brazing and soldering |  |  | 
© Wallingford

## Slide 4: Box joints (1)
Box joints are used to construct carcasses. Carcass constructions include cupboards, drawers and bookcases.
Examples of box joints include:
butt joint (A, B, C, D)
corner rebate joint (A)
finger or comb joint (A)
dovetail joint (A)
dowel joint (A, B, C, D)
biscuit joint (A, B, C, D)
housing joint (A, B, C, D).
© Wallingford

## Slide 5: Box joints (2)
Butt joint – is the simplest and quickest to construct; however, it is not very strong.
It can be reinforced by dovetail nailing and corner blocks.
Corner rebate or lap joint – is stronger than a butt joint, because of the increased gluing area; however, it is still not very strong.
It can be reinforced by dovetail nailing.
© Wallingford

## Slide 6: Box joints (3)
Finger or comb joint – is stronger than a butt joint because of the mechanical connection and the increased gluing area.
Finger joints were developed by the furniture industry as a more efficient method of mass production.
Dovetail joint – is the strongest carcass joint, thanks to the complex mechanical connection and the significantly increased gluing area.
Dovetail joints can only be assembled in one direction, and can therefore only be pulled apart in one direction, making them particularly good when constructing drawers.
© Wallingford

## Slide 7: Box joints (4)
Dowel joint – is suitable for both corner and tee joints.
It is a particularly useful joint when working with chipboard and MDF.
Dowels are often combined with KD fittings such as cam locks in flat-pack furniture.
© Wallingford

## Slide 8: Box joints (5)
Biscuit joint – is used to join manmade boards.
A biscuit jointer cuts slots in both halves to be joined, into which an elliptical-shaped biscuit is inserted to make a mechanical connection.
The biscuits are elliptical pieces of timber that have been dried and compressed.
Once the glue is applied, the biscuit swells and reinforces the joint.
Biscuit joints are used extensively in commercial furniture manufacture.
© Wallingford

## Slide 9: Box joints (6)
Housing joint – is used to secure shelves and partitions in carcass constructions.
A through housing is the simplest to construct.
If it is desirable that the joint does not show, a stopped housing can be used.
If there is a danger of the joint being pulled apart, the dovetail housing provides additional lateral strength. They can be through or stopped.
© Wallingford

## Slide 10: Frame joints (1)
Frame joints fall into two broad groups: flat frame joints and three-dimensional frame joints.
Flat frame joints are used to construct picture frames, door frames and window frames.
Joints used in the manufacture of flat frames include:
– butt joint (A, B, C)
– mitre joint (D)
– halving joint (A, B, C)
– bridle joint (A, B )
– mortise and tenon joint (A, B, C)
– dowel joint (A, B, C).
© Wallingford

## Slide 11: Frame joints (2)
Three-dimensional frame joints are used to construct tables, chairs, beds and buildings where three or more pieces of timber meet.
Joints used in the manufacture of three-dimensional frames include:
– halving joints (C)
– bridle joints (C)
– mortise and tenon joints (A, B, C)
– dowel joints (A, B, C).
© Wallingford

## Slide 12: Frame joints (3)
Butt joint – is the simplest and quickest to construct; however, it is not very strong. It can be reinforced by dovetail nailing and corner blocks.
Mitre joint – is made by cutting both pieces to be joined at the same angle – 45° for a square or rectangular frame.
No end grain is shown.
The mitre can be reinforced by nailing, or by the insertion of veneer keys into saw cuts made across the joint.
© Wallingford

## Slide 13: Frame joints (4)
Halving joints – are stronger than butt joints, thanks to the increased gluing area.
They can be reinforced by dovetail nailing, screwing or dowelling.
Halving joints are made by removing half of the material thickness from both pieces at the point where they intersect.
Halving joints can be used to make corner, tee and cross joins.
© Wallingford

## Slide 14: Frame joints (5)
Bridle joints – are stronger than halving joints, thanks to the increased gluing area.
They can be reinforced by dovetail nailing, screwing or dowelling.
Bridle joints are made by removing the material thickness in thirds from both pieces at the point where they intersect.
Bridle joints can be used to make corner and tee joins.
© Wallingford

## Slide 15: Frame joints (6)
Dowel joints – are butt joints reinforced with dowel pegs.
They are strong, thanks to the mechanical connection and the increased gluing area.
Dowel joints are made by drilling holes equal to the diameter of the dowel being used in both pieces of material, at the point where they intersect.
If several joints are to be made, it is advisable to use a jig to speed up the process and ensure the holes line up.
Dowel joints can be used to make corner and tee joins.
© Wallingford

## Slide 16: Frame joints (7)
Mortise and tenon joints – are stronger than halving joints, thanks to the increased gluing area.
They can be reinforced by dowelling or, in the case of a through mortise, it can be wedged.
Mortise and tenon joints are made by removing the material thickness in thirds from both pieces at the point where they intersect.
Mortise and tenon joints can be used to make corner and tee joins.
When the joint is to be made at the end of a piece of timber, a haunched joint is used.
The sloping haunch is not visible when it is glued together.
© Wallingford

## Slide 17: Edge-to-edge joints
Edge-to-edge joints – are used to join planks of natural timber edge to edge, and to add a more attractive lipping to the edge of manmade boards.
When joining natural timber boards edge to edge, the edges must be planed true.
By alternating the curve displayed on the end grain, the distortion caused by cupping is reduced.
© Wallingford