## Slide 1: Joining Materials - Adhesives
Ian Bark & Lloyd Ansell
Series Editor: Louise T Davies

## Slide 2: Introduction
Methods of joining materials fall into two broad groups:
Semi-permanent – can be disassembled without damaging the material or the method of joining.
Permanent – cannot be disassembled without damaging the material or the method of joining.
© Wallingford

## Slide 3: Permanent joining methods
 | Timber | Metal | Plastic
Adhesives |  |  | 
Nails |  |  | 
Rivets |  |  | 
Box joints |  |  | 
Frame joints |  |  | 
Edge-to-edge joints |  |  | 
Rebates and grooves |  |  | 
Sheet metal joints |  |  | 
Welding |  |  | 
Brazing and soldering |  |  | 
© Wallingford

## Slide 4: Adhesives (1)
All joints that are made using adhesives are permanent.
There are many different types of adhesive for use on different materials and in different situations.
Adhesives will work only if the correct one for the job is used, and if the surfaces to be joined are clean, free from dust and grease.
Health and safety
Many adhesives give off toxic fumes and should only be used in well-ventilated areas.
© Wallingford

## Slide 5: Adhesives (2)
The table below shows which adhesives should be used with which material.
 | Timber | Metal | Plastic | Fabric
Timber | PVA or synthetic | Contact adhesive | Contact adhesive | PVA
Metal | Contact adhesive | Epoxy resin | Contact adhesive | Contact adhesive
Plastic | Contact adhesive | Epoxy Resin | Solvent cement | Contact adhesive
Fabric | PVA | Contact adhesive | Contact adhesive | Latex
© Wallingford

## Slide 6: Adhesives (3)
PVA (polyvinyl acetate) is the most commonly used wood glue.
It is a water-based adhesive, and works by soaking into the surface of the timber and setting when the water has been absorbed.
It is supplied in liquid form, ready to use; it is easy to apply, non-staining, and produces a strong bond.
Exterior-grade PVA must be used if there is a risk of the joint getting wet.
© Wallingford

## Slide 7: Adhesives (4)
Synthetic resin (Cascamite) is a stronger wood glue than PVA, and is also waterproof.
It is supplied in powder form, and has to be mixed with water.
When it has cured it forms a very strong, hard, brittle bond.
© Wallingford

## Slide 8: Adhesives (5)
Epoxy resin (e.g. Araldite) is an expensive adhesive that could be used to stick almost any clean and dry materials to each other.
However, because of the high cost it tends to be used for special purposes.
A resin and hardener are mixed together in equal amounts, and hardening begins immediately.
The adhesive is fully cured after several hours.
It makes an extremely strong and hard bond.
© Wallingford

## Slide 9: Adhesives (6)
Solvent cement (e.g. Tensol) works by dissolving the hard surface of hard plastics such as acrylic and high-impact polystyrene.
© Wallingford

## Slide 10: Adhesives (7)
Contact adhesive (e.g. Evostik) is used for gluing sheet materials such as melamine to work surfaces.
It works by applying it to both surfaces and allowing them to become touch dry.
Adhesion takes place as soon as the two surfaces make contact and there is no opportunity for repositioning – so get it right first time or else!
© Wallingford

## Slide 11: Adhesives (8)
Latex (e.g. Copydex) is used to bond paper, card and fabrics.
Hot-melt glue is applied using a glue gun, which melts the glue stick.
It is useful for modelling, but is of limited use otherwise.
© Wallingford